## Slide 1: WF on clarification for the definition of the UL duty cycle
OPPO
3GPP TSG-RAN WG4 Meeting #94-e-bis R4-2005211
Electronic Meeting, 20 – 30 Apr., 2020

## Slide 2: Background
The maxUplinkdutycycle-FR2 was defined in Rel-15 to help UE solve MPE issue. And, it was considered unclear because there is no definition of reference power which this capability is defined.
In RAN4#94e meeting, it was agreed to clarify that the UE maximum transmission power is used as a reference in the definition of the UL duty cycle. And the detailed definition of “UE maximum transmission power” will be further discussed in RAN4#94e-bis meeting.

## Slide 3: WF
maxUplinkdutycycle-FR2 is defined under the maximum transmission power. There is different understanding on the definition of “maximum transmission power”
  Option 1: Defined at max peak EIRP
  Option 2: Defined at max TRP
  Option 3: Is only valid for the reference PCMAX,ref, where PCMAX,ref is the PCMAX,f,c without using MPR, AMPR and PMPR
  Option 4: where UE creates largest power density for the critical part of the device surface or applicable proximity of the devices surface
Further clarification on Option 2(defined at max TRP) is needed regarding “Pcmax.f.c is defined as peak EIRP and PHR is also calculated as peak EIRP. So NW cannot know TRP value that UE uses and how NW utilize this UL duty cycle capability defined as max TRP?”
It is up to network implementation whether this capability can also be applied to lower power levels other than the maximum transmission power in Rel-15.