## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e-bis Reno, USA, November 18 -22, 2019
Ericsson, […]
WF on Rel-16 MTC RRM requirements
R4-2005288

## Slide 2: Preconfigured UL resource
In current agreements Tsearch is FFS when the UE is not configured with eDRX [R4-1907733]. Tsearch is the time required for performing tracking loop.
Proposals for Tsearch in normal DRX
  Option 1: Tsearch = 5 SF in normal coverage and enhanced coverage
  Other options are not precluded.

## Slide 3: Mobility enhancement: RSS based RSRP measurement for UEs
Conditions for RSS based RSRP measurement in IDLE mode serving cell measurements:
  if the RSS of serving cell share the same NB as that of paging occasion MPDCCH for successive DRX cycles, and
  at least two RSS subframes exists immediately before the first subframe of paging occasion MPDCCH, for successive DRX cycles
    FFS on at least two subframes exists immediately after the last subframe of paging occasion
    (FFS: min/max distance of start/end of RSS occasion w.r.t end/start of MPDCCH), and
  RSS power offset with respect to CRS is equal to or greater than 0 dB, and
  RSS-based measurement period is not longer than CRS-based measurement period, definition of measurement period in IDLE mode will be discussed further in 2nd round.
Conditions for RSS based RSRP measurement in IDLE mode neighbor cell measurements:
  RSS power offset with respect to CRS is equal to or greater than 0 dB, and
  at least two RSS subframes exists immediately before the first subframe of paging occasion MPDCCH, for successive DRX cycles
    FFS on at least two subframes exists immediately after the last subframe of paging occasion
    (FFS: min/max distance of start/end of RSS occasion w.r.t end/start of MPDCCH), and
  FFS on whether the UE is expected perform concurrent measurements on CRS and RSS.
  FFS on RSS from neighbour cell is within same 2-RB layer as serving cell RSS

## Slide 4: Mobility enhancement: RSS based RSRP measurement for UEs
Measurement delays in IDLE:
  RSS-based measurement period is not longer than CRS-based measurement period
  Nserv as measurement period for serving cell
  Whether to use Tmeasure or Tevalute is FFS for neighbour cells.
Measurements in CONNECTED mode
  RSS power offset with respect to CRS is equal to or greater than 0 dB
  RSS can colllide with measurement gap, but UE is not expected do any RSS measurement within the gap. Instead the UE can measure in the subframes before and after the gap.

## Slide 5: Mobility enhancement: RSS based RSRP measurement for UEs
RSS measurement accuracy requirements are to be specified by averaging the simulation results (excluding RF margin) and a fixed RF margin is added on top.
For the RF margins, following options are under consideration:
  Non-BL UE
    2.5 dB
  BL UE
    Option 1: 3 dB
    Option 2: 4 dB

## Slide 6: MPDCCH performance improvement for RLM
Enhanced MPDCCH is used:
  When enhanced RLM E1 event is triggered
  When in normal RLM OOS is triggered
Other interested companies are encouraged to provide simulation results for the this scenario for RAN4#95-e meeting based on agreed simulation assumptions (ref. R4-1914343).

## Slide 7: DL quality reporting
RAN4 shall wait for RAN2 conclusion regarding reporting table for 2-bit and 3-bit reporting.
If RAN2 agrees to introduce 2-bit and 3 bit reportings, options for reporting tables to be considered include following (see next slide).

## Slide 8: DL quality reporting
Option for reporting table for 2-bit reporting
Option for reporting table for 3-bit reporting
Other options are not precluded.
 | Rmax | 1 or 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
Value 1 | Rmax / 8 | 1 | 1 | 1 | 2 | 4 | 8 | 16 | 32
Value 2 | Rmax / 4 | 2 | 2 | 2 | 4 | 8 | 16 | 32 | 64
Value 3 | Rmax | 4 | 4 | 8 | 16 | 32 | 64 | 128 | 256
Value 4 | 4 x Rmax | 8 | 16 | 32 | 64 | 128 | 256 | 256 | 256
Configured Rmax | Rmax <= 16 | Rmax >= 32
Value 1 | No measurement reporting | No measurement reporting
Value 2 | 1 | 4
Value 3 | 2 | 8
Value 4 | 4 | 16
Value 5 | 8 | 32
Value 6 | 16 | 64
Value 7 | 32 | 128
Value 8 | 64 | 256