## Slide 1: WF on R16 NR RRM enhancements – CGI reading
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, Apr. 20th – Apr. 30th 2020
R4-2005344

## Slide 2: Agreements in the meeting
UE is not required to meet L3 RRM measurement requirements during CGI reading
UE is not required to meet L1 RRM measurement requirements during CGI reading
1 sample for AGC/AFC is assumed for MIB decoding
The interruption core requirements for CGI reading of NR cell is specified by interruption numbers and interruption length
  Up to X interruptions of duration up to K1 for MIB decoding and additionally up to Y interruptions of up to K2 for SIB decoding
  How frequently each interruption happens during SIB1 decoding
  20ms for multiplexing pattern 1
  SMTC period for multiplexing pattern 2/3
MIB decoding and interruption
  SSB selection procedure is up to UE implementation
    UE may search the best one of all the SSBs within SMTC window
    UE may use SSB with the same index as the one with best RSRP in L3-RSRP report
  RX beam for FR2
    Option 1: The RX beam for the reported best RSRP is used
    Option 2: UE searches the best Rx beam
  Interruption is 6ms gap length

## Slide 3: WF on MIB decoding
MIB decoding delay for FR2
  Option 1 : [5] * TSMTC, where TSMTC is SMTC periodicity of target cell.
  Option 2 : [5] * N * TSMTC, where N = 8 and TSMTC is SMTC periodicity of target cell.
  Note: Depending on outcome of if RX beam sweeping is needed for MIB decoding.

## Slide 4: WF on SIB1 decoding
How is the SIB1 decoding delay to be derived
  Option 1a :
    Soft combining of 4 samples at -6dB SNR without side condition on scheduling periodicity and assuming soft combining across scheduling period boundaries
    [4] samples
  Option 1b
    Assumption is soft combining of 4 samples at -6dB SNR without side condition on scheduling periodicity and assuming soft combining across scheduling period boundaries
    [6] samples
  Option 2a
    One shot at -3dB SNR
    [4] samples
  Option 2b
    One shot at -3dB SNR
    [7] samples
  Option 3
    Soft combining of 2 samples at -6dB SNR with side condition that no requirements for 160ms SIB1 scheduling periodicity
    [7] number of samples
  Option 4
    Further evaluate the SIB1 reading performance for the case of AWGN and interference limited conditions (e.g. colliding SIB1 transmissions in the serving and neighbor cells)
    Further identify typical scenarios for CGI reading in terms of SIB1 collision between serving and neighbor cells

## Slide 5: WF on interruption requirements
Interruptions for each autonomous gap during SIB1 decoding
  2 slots (target cell SCS) + margin for multiplexing pattern 1
  7 symbols (target cell SCS) + margin for multiplexing pattern 2/3
  Margin
    Option 1: 2*RF tuning time + 1 slot (victim cell SCS)
    Option 2: 2*BWP switch delay + 1 slot (victim cell SCS)

## Slide 6: WF on known cell conditions
FFS if known cell conditions is needed based on agreements that SSB selection is up to UE implementation.
FFS how to specify known cell conditions if necessary.