## Slide 1: WF on CBW for REFSENS testing and alignment of configuration parameters for NR V2X
Vodafone
3GPP TSG-RAN WG4 Meeting #94bis-e
Electronic Meeting, April 20 – 30 2020
Draft R4-2005642

## Slide 2: Background (BW Testing) 1/2
A TBD item in R4-2002789 is the operation bandwidth for LTE Uu and SL to be used for Rx sensitivity testing.
Therefore, 10 MHz was proposed in R4-2003383, as this seems typical for B20 cellular deployments and 10MHz channel bandwidth on sidelink would match the nominal channel size of n47.
During phase 1 (see summary for Issue 1-3, R4-2005693), it was commented: “Cannot proceed as choice of 10 MHz for REFSENS testing instead of other bandwidths (e.g. 5 MHz, 20 MHz) not understood”.
To answer this point, from Vodafone perspective, the aim was that aligning to n47 channel bandwidths initially could make device implementation simpler. However, in principle not against more flexibility.

## Slide 3: Background (Key Config Parameters) 2/2
It was highlighted that there are lots of potential configuration parameters for NR V2X, and that it may be useful to advise 5GAA of this, given that some harmonisation of device implementations may be needed with respect to these parameters.
During the Phase 1 discussion, this seemed to be agreeable – on the understanding that a response from 5GAA should not be a pre-requisite for completion of the 3GPP Release 16 NR V2X work item.

## Slide 4: Proposal
Based on this, the following is proposed for Issue 1-3:
  NR V2X REFSENS tests for the B20 + n38 combination are performed for 10 MHz and 20 MHz mirroring the requirements of 36101 – other BWs are FFS
  Inform 5GAA of the range of configuration options we are defining for NR V2X sidelink within RAN4 specs, in terms of channel bandwidth, numerology, and frequency bands, and that further industry alignment may be useful to aid interoperability.
    This may be highlighted as part of an overall LS informing 5GAA of the completion of the NR V2X work item – which we assume will be sent from RAN#88e.