## Slide 1: WF on intra-band UL contiguous CA MPR
Skyworks, Huawei, HiSilicon, Qualcomm
3GPP TSG-RAN WG4 Meeting #94-bis-e R4-2005658
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: Background based on [1] and scope
UL contiguous CA requested configurations are both B (100MHz) and C class (200MHz)
1PA/1LO architecture is assumed up to 200MHz aggregated bandwidth
2LO/2PA architecture is not precluded to circumvent BW limitations at the PA, TRX or BB generator level
In case of 2PA/2LO needed, 2PA architecture should be signaled and UL MIMO is not supported
Scope: Defining assumptions for MPR evaluation

## Slide 3: Background on waveforms
There is up to 2dB difference in PAPR for DFT-s-OFDM and CP-OFDM between correlated and user data only uncorrelated case
It is essential to use different data input for each CC to avoid correlated peaks in each CCs especially when LCRB is the same in each CC.
If single or separate waveform generator are used it is enough to use different PRBS sequences (PN9 and PN23 for example) per CC. Cell ID is the same for each CC
Lower correlation can further be obtained by using different DMRS patterns for each CC (RB shift) and may be considered

## Slide 4: Background on contiguous inner/outer from [2]
For Aggregated channel bandwidth≤200Mhz (class B and Class C)
For RBStart,Low = max(1, floor(NRB_alloc /2)), where NRB_alloc=LCRB1*2^µ1+LCRB2*2^µ2
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤ceil[(1/2NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB2*2^µ2
RBStart = RBStart1 ∙ 2^µ1, if LCRB1 > 0
RBStart = NRB1 ∙ 2^µ1 + RBStart2∙2^µ2, if LCRB1 = 0
Other RB allocations are outer RB allocation.

## Slide 5: Background on non-contiguous inner from [2]
Inner allocations are for (IM3 fall within BW_CA region):
For RBStart,Low = max(1, floor(NRB_alloc)),
where NRB_alloc = LCRB2 ∙ 2^µ2, if LCRB1=0
NRB_alloc = LCRB1 ∙ 2^µ1, if LCRB2=0
NRB_alloc = (NRB1- RBStart1) ∙ 2^µ1 + (RBStart2+ LCRB2) ∙ 2^µ2+BWgap/0.18MHz, otherwise
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤Floor[(1/3NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB2*2^µ2+(BWgap+2*BWGB) /0.18MHz
RBStart = RBStart1 ∙ 2^µ1, if LCRB1 > 0
Where BWgap=Nominal channel space-(NRB1*12*SCS1/2+ NRB2*12*SCS2/2+(SCS2-SCS1)/2)

## Slide 6: Background on non-contiguous outer1/2 from [2]
Outer 1 allocations are for (IM3 and IM5 fall in 0 to BW_CA FOOB region):
NRB_alloc = (NRB1- RBStart1) ∙ 2^µ1 + (RBStart2+ LCRB2) ∙ 2^µ2+BWgap/0.18MHz
NRB,agg=NRB1*2^µ1+ NRB2*2^µ2+(BWgap+2*BWGB) /0.18MHz
2* NRB_alloc< RBstart1*2^µ1+ NRB,agg
2* NRB_alloc< (NRB2-(RBstart2+LCRB2))*2^µ2 +NRB,agg
Other allocations that are not inner or outer 1 allocations are outer 2 allocations

## Slide 7: WF on MPR evaluation assumption
Post PA losses of 4dB
PA calibrated for 30dB ACLR at 26dBm for 20MHz DFT-s-OFDM QPSK 100RB0 waveform
Appropriate waveform settings is used for PAPR
ACLR, SEM and spurious emission evaluated per agreements with associated bandwidth definitions in [1]
IBE and EVM are evaluated with two active CCs and RB allocation only on one CC thus single CC inner allocation MPR applies accordingly

## Slide 8: WF on cases to be evaluated - allocations
For contiguous allocation
  Whether Inner and outer allocation with potential relaxation for outer in class C for large allocation (either in terms of absolute allocated BW or in terms allocation ratio) FFS
  Whether Contiguous inner for class B and call C should have similar values (e.g. within ~1dB) FFS
For non-contiguous allocation
  Group into Inner, outer 1 and outer2 allocations
  Contiguous inner for class B and call C should have similar values (within ~1dB)

## Slide 9: WF on cases to be evaluated - others
Both DFT-s-OFDM and CP-OFDM
All modulation orders
20+20MHz and 50+50MHz (both 15kHz SCS) for class B
60+100MHz and 100+100MHz (both 30kHz SCS) for class C
MPR is reported for contiguous inner and outer allocations for class B and class C
MPR is reported for contiguous inner and outer1/2 allocations for class B and class C
In cases where MPR are equivalent MPR table may be merged

## Slide 10: WF on MPR table template and MPR value – contiguous allocations
Modulation |  | MPR for bandwidth class B |  | MPR for bandwidth class C | 
 |  | inner | outer | inner | Outer(1)
DFT-s-OFDM | Pi/2 BPSK | TBD | TBD | TBD | TBD
 | QPSK | [0-1.5]dB | [2-4]dB | [0-2.5]dB | [8]dB
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
CP-OFDM | QPSK | [1.5-3]dB | [3~5]dB | [1.5-4]dB | [8]dB
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
In cases where MPR are equivalent MPR table may be merged
(1) this is the worst case value and whether some lower value may be proposed conditioned on allocation ratio or allocated BW in MHz FFS

## Slide 11: WF on MPR table template and MPR value– non-contiguous allocations
In cases where MPR are equivalent MPR table may be merged
Modulation |  | MPR for bandwidth class B |  |  | MPR for bandwidth class C |  | 
 |  | inner | Outer1 | Outer2 | inner | Outer1 | Outer2
DFT-s-OFDM | Pi/2 BPSK | TBD | TBD | TBD | TBD | TBD | TBD
 | QPSK | [3]dB | [6]dB | [13]dB | [4]dB | [6]dB | [14]dB
 | 16QAM | TBD | TBD | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD | TBD | TBD
CP-OFDM | QPSK | [4]dB | [7]dB | [13]dB | [4]dB | [7]dB | [14]dB
 | 16QAM | TBD | TBD | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD | TBD | TBD

## Slide 12: Reference
[1] R4-2005657, “WF on intra-band UL contiguous CA general requirements”, Huawei, […]
[2] R4-2005100, “Email discussion summary for RAN4#94be_#14_NR_RF_FR1_Part_1”, Huawei