## Slide 1: WF on timing mask requirement for ULSUP-TDM
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #94-e BIS
Online, 20th – 30th April, 2020
R4-2005663

## Slide 2: Background
In RAN4#94e and #94e-Bis meetings, the following questions for timing mask requirement for ULSUP-TDM were discussed:
  Sub-topic 5-1: Should the uplink timing difference between LTE and NR up to BS TAE+Tae be considered for ULSUP-TDM?
    Q1: In order to address the original question for sub-Topic 5-1, i.e., should the uplink timing difference between LTE and NR up to BS TAE+Tae be considered for ULSUP-TDM, more evaluation including simulation seems be needed. Then if needed, what is the assumption for simulation or evaluation?
    Q2: Is the condition under which the present time masks apply clear, or should the clarification on the condition be needed?
    Q3: If the agreed answer to Q1is yes, how should the condition be clarified?
  Sub-topic 5-2: How to capture the impact of uplink timing difference on the core specifications for ULSUP-TDM?
    Q1: Should the discussion be postponed due to RAN2 on-going discussion on the applicability of the capability ul-SharingEUTRA-NR (related to ULSUP-TDM) for variable duplex bands?
    Q2: Is there any UE behavior which needs RAN1 feedback?
  Sub-topic 5-3: Whether and how to test the time mask

## Slide 3: Way forward
  The key issue is sub-topic 5-1. In order to address this issue, it is proposed to provide the simulations to do the evaluation for Q1 and Q2 in sub-topic 5-1
    Run link level simulation to evaluate the impact of uplink timing difference on the BS demodulation performance
      Assume one LTE user and one NR user adjacent to each other in frequency domain in the same uplink time slot with the following parameters:
        Follow the assumptions in Section 8.2.5 of TS38.104 ( which is NR requirements for UL timing adjustment) except for
          Propagation condition: Replace propagation condition for each user by TDLC300-100 Low, 1x2
          Uplink timing difference at the BS receiver between LTE and NR users: 5us, 3us, 2us, 1us, 0us
          MCS-s:
            LTE (16QAM, coding rate: 3/4, 25PRB, TM1), NR G-FR1-A4-8 (16QAM, coding rate: 658/1024, 25PRB, 15KHz SCS)
            LTE (64QAM, coding rate: 5/6, 25PRB, TM1), NR G-FR1-A5-8 (64QAM, coding rate: 567/1024, 25PRB, 15KHz SCS)
            LTE (256QAM, coding rate: 5/6, 25PRB, TM1), NR (256QAM, coding rate: 841/1024, 25PRB, 15KHz SCS)
          BS receiver: single FFT as baseline
        Provide the simulation results for both LTE and NR users assuming that BS receive both at the same time