## Slide 1: Way forward on LTE UE and BS performance requirements for additional enhancements for NB-IOT
Huawei,Hisilicon
R4-2008759
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2
Define NPDSCH performance requirements with multi-TB scheduled transmission by using the following simulation assumptions.
NPDSCH performance requirements
Parameter | Value
System bandwidth | 200 kHz
Operation mode | Stand alone
Antenna configuration | 1T1R
Channel model | ETU 1Hz
Frequency error | 0 Hz
Timing error | 0μs
Performance target | SNR@70% of maximum throughput
NSF | 10
Repetition number | 32
Transmission mode | Interleaved
HARQ process | 2
Carrier Type | Non-anchor
TB size | 1032
Duplex mode | HD-FDD
Interested companies are welcome to provide simulation results in the next meeting

## Slide 3
NPUSCH format 1 performance requirements
Parameters | Value
Number of tones | 12
SCS | 15kHz
Antenna configuration | 1T2R
Channel model | ETU 1Hz
Frequency error | 0Hz
Timing error | 0μs
Performance target | SNR@ 70% of maximum throughput
NRU | 5
Repetition number | 64
HARQ process | 2
Transmission mode | Interleaved
TB size | 424
Interested companies are welcome to provide simulation results in the next meeting
Define NPUSCH format 1 performance requirements with multi-TB scheduled transmission by using the following simulation assumptions.