## Slide 1: WF on IAB-MT output power dynamic
Qualcomm Incorporated
R4-2008775
3GPP TSG-RAN WG4 Meeting # 95-eis
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background
Dynamic range should guarantee that IAB-MT to parent link can maintain a certain level of performance under different conditions
  Fading/shadowing, weather variation, etc

## Slide 3: Way Forward
Dynamic range requirements:
  two separate requirements X and Y as following
Dynamic range (X)-dynamic PSD: power difference between min TX and max Tx power under the same side condition with full RB transmission.
- The side condition including modulation order, reference channel FFS
Dynamic range (Y)-constant PSD: 10*logNRB
  This applied for power ration among single RB and full RB in the same channel
FFS for the conformance test case design
Capture the dynamic range with below defintion with FFS on specified reference condition
  Option 1:The power dynamic range is the difference between the maximum and the minimum output power for a specified reference condition.
    NOTE: The upper limit of the dynamic range is the BS maximum output power with full RB transmission
  Other options not excluded

## Slide 4: Way Forward
For WA IAB-MT
  FR1 – X= 5dB
  FR2 – X= 5dB
  No additional power control requirements beside dynamic range requirements will be defined in Rel-16.
    FFS how the dynamic range requirements can guarantee the accuracy not only minimum threshold, which can be further discussed in performance phase.
For LA IAB-MT
  FR1 – X= 10dB
  FR2 – X= 10dB
  Introduce power control requirements, FFS for the details