## Slide 1: WF on transmit signal quality
CATT
3GPP TSG-RAN WG4 Meeting #95-e R4-2008783
Electronic Meeting, 25 May – 5 June, 2020

## Slide 2: Background (1/2) - Frequency error
The following contributions were provided in RAN4#95e
  R4-2007402, frequency error requirement for IAB, ZTE
  R4-2007573, IAB-MT Frequency error, Ericsson
  R4-2006799, RAN4 implication due to Sync from multiple parents for “Case 1” OTA timing, Samsung
The synchronization source issue and the spec impact were discussed in the meeting.
There was also a proposal to send LS to RAN1/RAN2 on the signaling aspect.

## Slide 3: Background (2/2) - Transmit modulation quality
The followings are the agreements related to IAB-MT transmit modulation quality before RAN4#95e
  EVM
    Re-use UE EVM requirements, excluding the low output power range, do not define PI/2 BPSK support for IAB-MT. Introduce QPSK, 16QAM, 64QAM modulation for both FR1 and FR2 and 256QAM only for FR1.
  Carrier leakage, In-band emissions
    IAB-MT In-band emissions, carrier leakage and image rejection shall be specified at maximum power level.
    The requirement in FR2 shall be
  EVM equalizer spectrum flatness:
    The zero-forcing equalizer used in EVM measurement shall meet the same flatness requirement as detailed in 38.101-1 and 38.101-2 for FR1 and FR2, respectively
In RAN4#95e R4-2006276 revisited the above agreements and EVM test procedure was also discussed in the same contribution.
Parameter description | Unit | Limit (NOTE 1) | Applicable Frequencies
General | dB |  | Any non-allocated RB
IQ Image | dB | -25 | Image frequencies
Carrier leakage | dBc | -25 | Carrier frequency
Parameter description | Unit | Limit (NOTE 1) | Applicable Frequencies
General | dB |  | Any non-allocated RB
IQ Image | dB | -25 | Image frequencies
Carrier leakage | dBc | -25 | Carrier frequency

## Slide 4: Way Forward (1/3) - Frequency error
frequency error requirement of IAB-DU in a child IAB node and frequency error requirement in its parent IAB-DU could be different. As such, whether the IAB-MT in a child IAB will be qualified as a synchronization reference for the IAB-DU in the same IAB has different opinions from companies:
  1. IAB-MT can be synchronization source of IAB-DU with condition of adding new signaling between parent IAB and child IAB.
    1-a: new signaling is needed
    1-b: existing signaling is ok, but out side the RAN4 group scope.
  2. IAB-MT can not be synchronization source of IAB-DU, additional spec impact need considered.
    Spec impact: In Rel-16, (R1-1903810) LS on OTA timing alignment for IAB is sent to RAN4 asking the T_delta granularity and RAN1 has agreed on the basic mechanism of over-the-air (OTA) timing alignment. So maybe there are some RAN1 spec related to such mechanism, this needs further check.
    Having a perfect time alignment between child IAB-DU and its pairing parent IAB-DU while violating the frequency requirement of child IAB-DU will not be acceptable from the regulator perspective.

## Slide 5: Way Forward (1/2) - Frequency error
It is proposed below options
Option 1: if RAN4 agree IAB-MT should not be used as synchronization source.
  LS to RAN1/RAN2 is needed
  Spec impact could be mentioned, but may be RAN1 spec.
Option 2 : IAB-MT can be used as synchronization source, but RAN4 decide up to implement in Rel-16 with below agreement;
  No LS on frequency error needed in this meeting
  No need to capture additional details to RAN4 specification
  No interoperability is guaranteed in Rel-16 and risk to violate the regulator requirement when different vendor IAB is mixed in the network should be minimized.

## Slide 6: Way Forward (2/2) - Transmit modulation quality
Wide area IAB-MT
  Option 1:
    No carrier leakage, in-band emission and EVM equalizer spectrum flatness requirements are defined for both FR1 and FR2.’
  Option 2:
    Keep the previous agreements for FR2 and do more study for FR1.
  EVM test procedure and FFS.
Local area IAB-MT
  FFS if carrier leakage, in-band emission and EVM equalizer spectrum flatness requirements will be defined and how to define them.
    Reusing current previous agreement is also an option.
  EVM test procedure FFS.