## Slide 1: Way forward on CA CQI reporting requirements
China Telecom
3GPP TSG-RAN4 Meeting #95e
Electronic Meeting, 25 May - 5 June, 2020
Agenda item: 6.18.1.5
R4-2008849
Document for: Approval

## Slide 2: Background: WF in previous meeting
RAN4 #94e-Bis
  WF: R4-2005548

## Slide 3: Test Parameters
Duplex mode and SCS combinations
  For the performance requirements:
    Option 1: Reuse the combinations from PDSCH normal
    Option 2:
      FR1: FDD + FDD with 15 kHz SCS and TDD + TDD with 30 kHz SCS
      FR2: TDD + TDD with 120 kHz SCS
  Applicability rule if option 1 for the performance requirements is agreed:
    Option 1: Test 2 of the 3 cases below, and FFS on the detailed applicability rule:
      Test #1: FDD 15 kHz + FDD 15 kHz
      Test #2: FDD 15 kHz + TDD 30 kHz, in case UE supports different SCS on different carriers for FDD-TDD CA, otherwise FDD 15 kHz + TDD 15 kHz
      Test #3: TDD 30 kHz + TDD 30 kHz, in case UE supports it, otherwise TDD 15 kHz + TDD 30 kHz
    Other options are not precluded

## Slide 4: Test Parameters cont’d
    Channel bandwidth and test applicability rule
  Decide in the next meeting on whether it is feasible to define CA CQI performance requirements in a bandwidth agnostic way.
  For the applicability rule:
    Option 1:
      For each agreed duplex mode and SCS combination for testing:
        » CA capability where the tests apply: Test any of one of the supported CA capabilities with largest aggregated CA bandwidth combination
        » CA configuration from the selected CA capability where the tests apply: Test any one of the supported CA configurations with largest aggregated CA bandwidth combination

## Slide 5: Test Parameters cont’d
  TDD pattern for 120kHz SCS
  Option 1: 3D1S1U with S=10:2:2
  Option 2: 2D1S1U with S=11:3:0
    CSI reporting periodicity for 120kHz SCS
  Depend on the agreement on TDD pattern for 120kHz SCS
    If TDD pattern of 3D1S1U is agreed, use 10 slots
    If TDD pattern of 2D1S1U is agreed, use 8 slots
Antenna configuration for CA CQI test
  1T2R and 1T4R
Signal power density for 2Rx and 4Rx requirements
  Option 1: For 4Rx requirements, reduce the signal power density by 3dB compared to that for 2Rx
  Use Option 1 as baseline, and it can be confirmed in the next RAN4 meeting if no technical concern will be observed.

## Slide 6: Test Metric
General principle
  Following the methodology used in LTE, the difference between the wideband CQI indices of Pcell and the first Scell as well as the difference between the wideband CQI indices of the first Scell and the other Scell(s) (if any) shall be not smaller than a threshold, for more than 90% of the time
  SNR configuration for 2DL CA CQI test
  Option 1: SNRPcell = 10dB and SNRScell = 4dB
  Other options are not precluded
  Make decision in the next meeting
  SNR configuration for 3 or more DL CA CQI test
  Option 1: SNRPcell = 12dB, SNRScell1 = 6dB, SNRScell2, 3,… = 0dB
  Other options are not precluded
  Make decision in the next meeting
    Delta CQI threshold for CA CQI test
  Option 1: thr = 2 for 2 or more DL CA
  Other options are not precluded
  Make decision in the next meeting

## Slide 7: Agreed test parameters in previous meeting
Parameter | Unit | Value
Propagation condition |  | AWGN
TDD pattern |  | For 30kHZ SCS: 7D1S2U with S=6:4:4
CSI reporting type |  | Periodic
CSI reporting periodicity |  | 5 slots for 15kHz SCS 10 slots for 30kHz SCS
CQI Table |  | For FR1: CQI Table 2 For FR2: CQI Table 1