## Slide 1: WF on the measurement interval and observation time for frequency/time correction for 2.5kHz and 0.37kHz
ZTE,
R4-2008869
3GPP TSG-RAN WG4 #95e
25th May. - 5th June. 2020

## Slide 2: Background
  In Rel-16 LTEbased 5G terrestrial broadcast, two numerologies 2.5KHz and 0.37KHz was introduced for mobility up to 250km/h and and rooftop reception, the basic diagram is shown as following:
  Similar as Rel-14 FeMBMS, EVM related issues for new introduced numerologies 2.5khz and 0.37khz should be specified. In the existing R16 TS 36.104 spec and R16 TS 36.101 spec, there are no such kind of requirement defined yet, therefore we proposed to further discuss and resolve it.
Figure 1. SCS 2.5kHz with CP 100us for mobility up to 250km/h
Figure 2. SCS 0.37kHz with CP 300us for rooftop reception

## Slide 3: Background
In 36.211, it states:
For subframes using Δf=2.5 kHz, , or , subframe is defined as two slots, and , of length each.
For subframes using , subframe is defined as one slot, , of length .
For transmissions using Δf=1⁄((82944T_"s" ) )≈0.37 "kHz" , a slot has a length of 92160T_"s" =3" ms" . There are 13 slots, numbered in increasing order from 0 to 12, in a 40 ms period starting at n_"f" " mod " 4=0 with slot 0 starting at 30720T_"s" in the 40 ms period

## Slide 4: WF
Basic unit of measurement scaling factor:
  Option 1: 1 slot per 38.104 definition
    2.5kHz SCS: 2 slots = 1ms
    0.37 kHz SCS: 1 slot = 3ms
  Option 2: other scaling factor
Measurement interval:
  Option 1:
    2.5kHz SCS: 10ms
    0.37 kHz SCS: 10ms
  Option 2: other

## Slide 5: WF
The observation period for determining the frequency/time offset
  Option 1: 1 slot per 38.104 definition
    2.5kHz SCS: 1 slots = 0.5ms
    0.37 kHz SCS: 1 slot = 3ms
  Option 2: scaling factor of 2
    2.5kHz SCS: 2 slots = 1ms
    0.37 kHz SCS: 2slot = 6ms
  Option 3: other

## Slide 6: WF
EVM window ratio and FFT size
for 2.5KHz and 0.37KHz SCS:
  EVM window ratio should reuse the value of 15KHz with normal CP;
  FFT size should only have factors of 2 and/or 3 basd on RAN1 agreement to limit UE complexity.

## Slide 7: References:
  [1]R4-2007396,Impacts on BS RF requirement of new introduced numerology, ZTE Corporation [2]R4-2007397,CR to 36.104: Introduction of LTE based 5G terrestrial broadcast numerologies
  [3]R4-2007398,CR to 36.101: Introduction of LTE based 5G terrestrial broadcast numerologies