## Slide 1: WF on remaining Rx RF requirements for NR V2X
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, 25 May – 5 June, 2020
Agenda item: 6.4.3.2
Document for: Approval
R4-2009170
CATT, LGE…

## Slide 2: Background
In RAN4#95-e meeting, the remaining issues on Rx RF requirements for NR V2X, including REFSENS, the maximum input level and ACS were discussed in the 1st round [1].
The diversity gain, noise figure in band n38, REFSENS target SNR level, ΔRIB,c for V2X_20_n38 and the maximum input level still need further discussion in the 2nd round.

## Slide 3: REFSENS: Diversity gain
  Diversity gain
  Option 1: Use a value of 2.5 dB for diversity gain for NR V2X REFSENS calculations.
  Option 2: Keep the previous agreements to define 3dB diversity gain.
  Companies preference
    Option1: Qualcomm
    Option2: LGE, Huawei, Futurewei, CATT
  Recommendations for 2nd round:
  Clarify whether the implementation loss of diversity gain is considered in the IM. If so, no need to consider implementation loss in diversity gain.
  Therefore, RAN4 can keep the 3dB diversity gain to consist with NR Uu.
  Qualcomm : Select option 1 as IM term only contains RF impairments and diversity gain implementation losses are not accounted in the IM term.
  Proposed WF by moderator: capture the REFSENS levels diversity gain with square brackets based on option 2.

## Slide 4: REFSENS: Noise figure in band n38
  Noise figure in band n38
  Option 1: Define NF of 13dBm for band n38 like band n47.
  Option 2: Keep the previous agreements to define NF of 9dB like NR Uu.
  Companies preference
    Option1: Qualcomm, CATT
    Option2: LGE, Huawei
  Recommendations for 2nd round:
  Discuss whether the additional 4dB increase in NF (9dB to 13dB) for n38 is required to compensate for the cable losses.
  The cable loss will be added in implementation loss not NF.
  Qualcomm: Select option 1: NF increase in n38 is required to compensate implementation cable losses in V2X vehicular applications.
  Proposed WF by moderator: FFS on NF in band n38.

## Slide 5: REFSENS: target SNR level
  Reference measurement channel and simulation assumptions for REFSENS target SNR level
  Option 1: Use the reference measurement channel and simulation assumptions to derive REFSENSE target SNR level based on R4-2006821 from Qualcomm.
  Option 2: Keep the previous agreements to define target SNR level as -1dB for REFSENS.
  Option 3: Capture the REFSENS levels by using target SNR level [-1] dB in this meeting. Interested companies could also bring simulation results in the future meetings based on the aligned simulation assumptions. If the target SNR level based on simulation results is not [-1] dB, the reference measure channel can be correspondingly revised to satisfy [-1] dB target SNR level.
  Recommendations for 2nd round:
  Option 3 can be agreed.
  Qualcomm: Select option 3 with square brackets around -1 dB. i.e. [-1] dB as indicated
  Proposed WF by moderator: Option 3 with the target SNR level [-1] dB captured.
Conclusion: REFSENS will be specified with previous agreements in TR38.886, then RAN4 can revisit the REFSENS according to technical discussion paper from next RAN4 meeting.

## Slide 6: ΔRIB,c for V2X_20_n38
  ΔRIB,c for V2X_20_n38
  Option 1: Use the HTF to reduce the 3rd harmonic impact into n38. ΔRIB,c is 0.2dB as use shared pain approach.
  Option 2: Keep the ΔRIB,c is TBD in TR.
  Option 3: A note should be placed either saying “No requirements apply for the case that there is at least one individual RE within the uplink transmission bandwidth of the relative higher band and when the frequency range of relative higher band’s uplink channel bandwidth or uplink 1st adjacent channel bandwidth is fully or partially overlapped with the 3 times of the frequency range of the relative lower band’s downlink channel bandwidth. The reference sensitivity is only verified when this is not the case” or a MSD number should be put into the spec to account for sensitivity degradation when 3rd harmonic of B20 falls into the operating band of n38. A trap filter cannot reduce the 3rd harmonic sufficiently to give only 0.2 dB of REFSENS degradation if a 3rd order harmonic from B20 falls inside band n38.
  Recommendations for 2nd round:
  The interference of the specific band combination, e.g. intermodulation in V2X_20_n38, should be further discussed in the 2nd round. It is preferred to derive a value of ΔRIB,c in this meeting.
  To remove TBD in specification, Option1 is chosen in this meeting. RAN4 can further check the delta value by HTF.
  Qualcomm: Select option 3, as ΔRIB,c =0.2dB is insufficient when harmonic falls in band.
  Proposed WF by moderator: FFS on ΔRIB,c for V2X_20_n38

## Slide 7: Maximum input level
  Maximum input level at n47
  Option 1: Follow the maximum input levels for NR Uu for 64QAM and 256QAM.
  Option 2: -25dBm for 64QAM and -27dBm for 256QAM applicable to all CBWs.
  Recommendations for 2nd round
  Option 1 (the majority view) can be agreed.
  If not, discuss whether the relaxation on the maximum input level for larger CBWs is needed.
  Compromise between option 1 and option 2, Relax 1 dB based on option 1 for 64QAM and 256QAM
  Qualcomm: Select option 1. The assumption has been that the SL and Uu links have similar performance, so it is reasonable to set the maximum input levels for SL based on what is used in NR Uu.
  Proposed WF by moderator: Capture the maximum input levels with square brackets based on option 1.

## Slide 8: Reference
[1] R4-2008302, Email discussion summary for [95e][112] 5G_V2X_NRSL_UE_RF_RX, Moderator (CATT), RAN4#95e
[2] R4-2006259, Discussion on remaining issues on Rx RF requirements for NR V2X, CATT, RAN4#95e
[3] R4-2006261, TP on remaining issues on Rx RF requirements for NR V2X, CATT, RAN4#95e
[4] R4-2006262, CR for TS38.101-1, Introduce Rx RF requirements for NR V2X single carrier, CATT, RAN4#95e
[5] R4-2006821, REFSENS issues in V2X, Qualcomm Incorporated, RAN4#95e
[6] R4-2008223, On remaining NR V2X Rx requirements, Huawei, HiSilicon, RAN4#95e
[7] R4-2006746, TP on remaining issues for NR V2X UE, LG Electronics France, RAN4#95e