## Slide 1: WF on intra-band UL non-contiguous CA UE capability
Huawei, HiSilicon, [ ]
R4-2008470
3GPP TSG-RAN WG4 #95-e
May 25th – June 5th, 2020
Electronic meeting

## Slide 2: Background
Why the current CA signaling is not sufficient for Rel-16 UL NC CA
NR intra-band UL NC CA can be supported by 1PA or 2PA architecture which is depending on the frequency separation. The UE may support the UL NC CA with different frequency separation with different PA architecture
  Frequency separation: the maximum bandwidth including CCs and the gap between CCs
UE need to report the max MIMO UE capability for 1PA architecture and 2PA architecture respectively
  When PA architecture capability changes for different frequency separation, the max MIMO capability maybe changed
    For 1PA architecture on CA support, UE need to have 2PA/Tx chain to support UL MIMO.
    For 2PA architecture on CA support, UE need to have 4PA/Tx chain to support UL MIMO.

## Slide 3: WF on Signaling on UL NC CA
Intra-band UL NC CA signaling
  Component 1: Maximum UL frequency separation
    Candidate frequency separation class: {100MHz, 200MHz, >200MHz}
    Whether more bit number need to reserved for frequency separation class FFS.
  Component 2: PA architecture
    On the condition that component 1 is indicated, indicate the PA architecture, i.e, 1PA or 2PA, default value aligned with Rel-15 signalling
  Component 3: max UL MIMO layer
    On the condition that component 1 and component 2 are indicated, indicate the MIMO layer number for each UL CC separately
CA configuration: 20MHz+20MHz
Separation class: 100MHz
PA Archi: 1PA
UL MIMO : 2 layer
Separation class: 200MHz
PA Archi: 2PA
UL MIMO: 1 layer
Separation class: >200MHz
PA Archi: 2PA
UL MIMO: 1 layer
Multiple sets of UE capability on one UL NC CA configuration can be indicated, which can clearly signal the changing UE capability on PA architecture for different frequency separation, and the max UL MIMO layer can be signaled due to different PA architecture.
One example for the signaling on UL NC CA

## Slide 4: WF on Signaling on UL NC CA
The signalling architecture for Intra-band UL NC CA is also applied for intra-band contiguous CA

## Slide 5: WF on Signaling on UL NC CA-RF requirement related
Intra-band UL NC CA RF requirement signaling
  Component 1: Indicate whether the in-gap ACLR and/or SEM need to be relaxed
    Only applicable for 1PA architecture
    The UE need to fulfill the relaxed RF requirement specified in TS 38.101
CA configuration: 20MHz+20MHz
Separation class: 100MHz
PA Archi: 1PA
UL MIMO : 2 layer
Separation class: 200MHz
PA Archi: 2PA
UL MIMO: 1 layer
Separation class: >200MHz
PA Archi: 2PA
UL MIMO: 1 layer
RF relax: {Yes,no}
One example for the signaling on UL NC CA