## Slide 1: WF on FR2 Beam Squint Effect
SONY, ….
3GPP TSG-RAN WG4 Meeting # 95-e draft R4-2008488
Electronic Meeting, 25 May – 5 Jun., 2020

## Slide 2: Background
Beam squint happens when DL BM reference signals and UL/DL control and/or data channels of interest are not within the same CC, see figure on right
Beam squint causes a received signal to have a frequency selective characteristic
  It is a radiative-domain impairment
  It causes gain droop, like impairment caused by active circuitry in the conducted domain
Problem statement: Given CC1 and CC2 separated by ∆f and assuming the UE uses the codebook entry optimized for CC1, what is the degradation of CC2 spherical coverage?
RAN4 has further discussed the impact due to beam squint effect on the requirement of CBM inter-band CA and intra-band CA 3GPP TSG-RAN WG4 Meeting # 95-e.
Difference in antenna gain, ‘x’ dB
gNB
UE
Conducted power in transmitted CCs
Ref signal for BM
Blue CC squints away from target direction due to separation in frequency from reference signal
Power received OTA
‘x’ dB

## Slide 3: WF on CBM inter-band DL CA and Intra-band DL CA
For EIS spherical coverage:
  If there will be EIS spherical coverage requirements for CBM inter-band DL CA: Including radiated relaxation due to the beam squint effect in the CBM inter-band CA EIS spherical coverage as below:
    For CBM inter-band CA EIS spherical coverage, allowing X dB relaxation (at spherical coverage point on CCDF) on the secondary CC.
    X depends on the frequency separation between primary and secondary CCs.
    The relaxation due to beam squint shall be included in the general inter-band CA relaxation.
  Intra-band DL CA: no impact to consider because spherical coverage requirement is absent.
  The following information shall be captured in the TR for information, based on company contributions
    CA EIS degradation quantified in terms of delta gain CDF, due to frequency separation from the CC configured as the beam management reference signal.
  Companies are encouraged to provide input on the value of X based on the agreed simulation assumption from R4-2005675 for the CBM inter-band CA spherical coverage requirement discussion
For REFSENS :
  The beam squint effect on the CBM inter-band REFSENS is FFS, companies are encouraged to verify if best EIS value is impacted.

## Slide 4: WF on Intra-band UL CA
The beam squint effect on the Intra-band UL CA is FFS, companies are encouraged to verify if there is impact to FR2 CA EIRP (peak and spherical coverage) for FS <= 1400 MHz

## Slide 5: WF on Beam management reference signal location for FR2 CA test
In FR2 CA cases, requirements apply when the BM RS is provided in a CC with a configured UL BWP
BM RS shall be provided in Pcell for CBM inter-band CA and intra-band CA. BM RS shall be provided in Pcell and one of Scell in IBM inter-band CA .

## Slide 6: Reference
R4-200XXXX Email discussion summary for [95e][123] NR_RF_FR2_req_enh_Part_3 Moderator (Qualcomm Incorporated)