## Slide 1: WF on NR bands to UL MIMO
Samsung, Skyworks
R4-2008895
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – Jun 5th 2020
Agenda: 6.21.2

## Slide 2
In RAN4 #94Bis-e, a way forward was approved for newly proposed NR operating bands (n1, n2, n3, n7, n30, n34, n38, n39, n40, n48 and n66, n70) for UL MIMO in UE PC3 power class [1]
  Accompanied draft CR was also endorsed with the proposed bands [2]
  MPR/A-MPR impacts to the new band for UL-MIMO is agreed to study in RAN4
CR is submitted to RAN4 #95-e with agreed changes and some editorial modifications. In addition, both n25 and n71 are added in the table of operating bands for UL MIMO which were not covered under [2]
No CR/Tdoc on addressing the release independence and A-MPR/MPR study is submitted to this meeting
Background

## Slide 3
RAN4 agrees the proposed CR to introduce an operating band list and NR bands to UL MIMO configuration [3]
  n71 is added only for FWA form factor UEs as NOTE 2
WF: Proposed NR Bands to UL MIMO
NR operating band
n1
n2
n3
n7
n25
n301
n34
n38
n39
n40
n41
n48
n66
n70
n712
n77
n78
n79
NOTE 1: Uplink transmission is not allowed at this band for UE with external vehicle-mounted antennas. NOTE 2: UL MIMO is targeted for FWA form factor.

## Slide 4
Study on MPR/A-MPR impacts to the NR bands for UL MIMO will be continued with following simulation assumptions
  Focus on OOBE, spurious emissions, and ACLR
  15 kHz SCS as 1st priority, other SCS secondary
  MIMO mode: 2x2 coherent UL MIMO
    Amplitude correlation of the two antenna waveforms is assumed
    MPR for 2 layer UL MIMO is FFS
  Use cases
    PC3 with 23+23dBm
    PC2 with 23+23dBm (Rel-15)
    PC1.5 with 26+26dBm (Rel-16): covered in the 29dBm WI, see R4-2008902
  Antenna isolation: 10dB for all band >1GHz and also for n71 for FWA UE
Companies are also encouraged to provide the input evaluated by measurements
WF: MPR/A-MPR Impacts

## Slide 5
[1] | R4-2005654 | WF on additional bands for UL-MIMO | 
[2] | R4-2005653 | dCR to 38.101-1: Introduce an operating band list and NR bands to UL MIMO configuration | 
[3] | R4-2008894 | CR to 38.101-1: Introduce an operating band list and NR bands to UL MIMO configuration | 
References