## Slide 1: WF on FR2 FWA evaluations
Qualcomm
3GPP TSG-RAN WG4 Meeting # 95-e R4-2008921
Electronic Meeting, 25 May – 5 June 2020

## Slide 2: Background
Japan FWA has unique design targets:
  Max. TRP of 23 dBm
  Max antenna gain of 20 dBi
  Peak EIRP and REFSENS suitable for FWA application
  Use cases like that of PC1, but modified for EIRP and REFSENS

## Slide 3: WF on peak EIRP
On how to determine appropriate value of min. peak EIRP
  Option 1: Identify target dBm values, no consideration for element count
    26, 28, 32, etc
  Option 2: Average company estimates to derive requirement after convergence on element count ‘N’
    N=8, N=16
  Option 3: Create multiple power classes that differ in min. peak EIRP value
    PC5 ~ 32 dBm
    PC6 ~ 28 dBm
  Option 4: Repurpose existing power classes with additional signaling
    Example: PC2 in ‘FWA condition’ is expected to produce +28 dBm of peak EIRP, and 8 dB degradation at 85th %ile

## Slide 4: WF on REFSENS
On how to determine appropriate value of REFSENS
  Option 1: Identify target dBm values for SNR of -1 dB, 50MHz channel , no consideration for element count
    Examples: -90.5, -91.5, etc,
  Option 2: Average company estimates to derive requirement
  Option 3: Average company estimates to derive requirement after convergence on element count ‘N’
    N=8, N=16
  Option 4: Pick highest REFSENS among proposals to derive requirement
    Highest REFSENS is most relaxed value that is inclusive of all proposals

## Slide 5: WF on Spherical Coverage
Japan FWA shall have no more than 8 dB degradation from peak value in 85th %ile direction.
  EIRP in 85th%ile direction (CDF) is min peak EIRP – 8 dB
  EIS in 85th%ile direction (CCDF) is REFSENS + 8 dB

## Slide 6: Reference
R4-2008326 Email discussion summary for [95e][136] NR_FR2_FWA_Bn257_Bn258 Moderator (Softbank Corp.)