## Slide 1: WF on inter-frequency without MG
CMCC
3GPP TSG-RAN WG4 Meeting # 95-e R4-200XXXX
Electronic Meeting, 25th May - 5th Jun 2020

## Slide 2: Background
R4-2005348 WF on inter-frequency without MG was agreed in RAN4#94e bis meeting
R4-2002250 WF on inter-frequency without MG was agreed in RAN4#94e meeting
R4-1915853 WF on inter-frequency without MG was agreed in RAN4#93meeting.

## Slide 3: Issue 2-1: Capability of supporting inter-frequency measurement without MG
  Optional with UE capability signaling

## Slide 4: Issue 2-2: Scheduling restriction when the target SSB has a different SCS grid
Do not define requirements for scenarios when the target SSB has a different SCS grid

## Slide 5: Issue 2-3-1: Relation between “NeedForGap” and “inter-frequency without MG”
If UE indicates “gap”, but UE indicates the support of “inter-frequency without MG”, UE can still be able to do gapless measurement when the target SSB is completely contained in UE’s active BWP.
If UE indicates “no gap”,
  Option 1: UE needs to also indicate the support of “inter-frequency without MG”, and the gap is not needed for measurement, regardless whether the target SSB is completely contained in UE’s active BWP or not.
  Option 2: the gap is not needed for measuring the concerned frequency, regardless of the new RAN4 gapless mechanism.

## Slide 6: Issue 2-3-2: On replied LS on NeedForGap capability (merged from thread#233 topic #6)
RAN4 to confirm that the NeedForGap signaling design is irrelevant independent with RAN4 ’s ongoing discussion on inter-frequency measurement without gap in Rel16 RRM enhancement WI.
Note: discussion on NeedForGap shall not impact the completion of R16 RAN4 inter-frequency without MG topic.