## Slide 1: Way Forward on ultra-low BLER requirements
R4-2008805
Moderator (Ericsson)

## Slide 2: Agreements in first round
For the UE, MCS 14 is agreed
For the UE, antenna assumption is changed to 1x2, 1x4
UE applicability agreement: Requirements are applicable for UEs that support both MCS Table 3 (dl-64QAM-MCS-TableAlt) and CQI Table 3 (cqi-TableAlt).
BS TDD pattern: 3D1S1U (S=10:2:2) for 15kHz, 7D1S2U (S=6:4:4) for 30kHz
X is confirmed as 0.5dB for the UE and 1dB for the BS
For the BS, the test applicability rule means that either typeA mapping or typeB mapping is tested (depending on declaration) but not both.

## Slide 3: Agreements in second round

## Slide 4: Open issues
Issue 1: CQI requirement
Proposals
  Option 1: No CQI requirement (Intel, Huawei, Apple)
  Option 2: CQI requirement with median CQI and BLER with higher/lower CQI followed, together with test applicability rule on CQI/FMCS (Qualcomm)
Recommended WF
Issue 2: FR2 requirements
Proposals
  Option 1: FR2 requirements (DoCoMo)
  Option 2: No FR2 requirements (Apple, Qualcomm, Ericsson, Huawei, Samsung)
  Option 3: Defer decision to next meeting (Intel, DoCoMo)
Recommended WF
  For the current discussion, it is recommended to discuss the general need for FR2 requirements rather than splitting into UE and BS discussions (due to the risk of splitting & repetition of comments)

## Slide 5: Open issues
Issue 1: How to capture X in UE specifications
Proposals
  Option 1: Capture implicitly in the core requirement (Huawei)
  Option 2: Capture in RAN5 specifications (Ericsson, Intel, Apple)
Recommended WF:
X is captured in the RAN5 specification. “Extra Margin” EM needed to ensure that the RAN4 requirement is suitable to achieve 10^-5 is discussed and captured implicitly in the core specification as usual in RAN4.

## Slide 6: Open issues
Issue 2: How to capture X in BS specifications
Proposals
  Option 1: Capture implicitly in the core requirement (Huawei)
  Option 2: Capture as addition to test requirement in conformance specifications, but separate to TT as follows (Nokia, Samsung, Ericsson, Intel, DoCoMo): <Table to be inserted>
Recommended WF:
Option 2 is used for specifying X. “Extra Margin” EM needed to ensure that the RAN4 requirement is suitable to achieve 10^-5 is discussed and captured implicitly in the core specification as usual in RAN4.

## Slide 7: Open issues
Issue 3: Number of UE test cases for FMCS requirement
Proposals
  Option 1: One test case
  Option 2: 4 test cases (Ericsson, Apple, Intel)
  Option 3: Any other proposals ?
Recommended WF
  Option 2
Issue 4: Test applicability for UE
Proposals
  Option 1: Test both FDD and TDD, max supported RX (Intel, Ericsson)
  Option 2: Test only one of FDD and TDD, max supported RX (Ericsson)
  Option 3: Any other proposals ?
Recommended WF
  Option 1

## Slide 8: Open issues
Issue 5: Test applicability rule for FMCS and CQI
Only applicable if CQI test is introduced
Proposals
  Option 1: Introduce applicability rule
  Option 2: No rule; both tested
Recommended WF
Issue 6: BS SCS test applicability
Proposals
  Option 1: All supported SCS tested (Ericsson, Intel)
  Option 2: Only 15kHz SCS tested if both supported (Ericsson, Nokia)
  Option 3: Only 30kHz SCS tested if both supported (Ericsson, Nokia, Intel)
Recommended WF
  Option 3 ?

## Slide 9: Agreed simulation assumptions (BS)
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Duplex mode |  | FDD/TDD
Antenna configuration |  | 1x2, ULA low 1x4, ULA low
PDSCH configuration | Mapping type | Type A
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PUSCH aggregation factor | 1
PDSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Number of HARQ Transmissions |  | 1
PT-RS |  | Disabled
Propagation condition |  | AWGN
MCS Table |  | Table 3, MCS14
SCS and BW |  | FDD:15KHz, 10MHz TDD:30KHz, 40MHz
Frequency domain resource |  | Full BW
TDD pattern |  | 7D1S2U (S=6:4:4)
Testing metric |  | Target BLER: 10-5

## Slide 10: Agreed simulation assumptions (UE)
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA low
PUSCH configuration | Mapping type | Type A and Type B
 | Starting symbol (S) | 0
 | Length (L) | 14
 | PUSCH aggregation factor | 1
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Number of HARQ Transmissions |  | 1
PT-RS |  | Disabled
Propagation condition |  | AWGN
MCS Table |  | Table 3, MCS 5
SCS and BW |  | 15 kHz for 10 MHz 30 kHz for 40 MHz
Frequency domain resource |  | Full Bandwidth
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
Testing metric |  | Target BLER: 10-5

## Slide 11: Agreements regarding testing
X is 0.5dB for UE and 1dB for BS
<Further agreements on how X is defined in specifications>
The RAN5 statistical test methodology is assumed, adapted for CL = 99.999%