## Slide 1: WF on BS demodulation requirements for 2-step RACH
ZTE
3GPP TSG-RAN WG4 Meeting #95-e
E-meeting, 25th May – 5th Jun, 2020
R4-2008864

## Slide 2: Background
Agreed WFs in previous meetings (Newest first)
  RAN4#94bis-e
    R4-2005555 WF on BS demodulation performance requirements for 2-step RACH
  RAN4#94-e
    R4-2002389 WF on BS demodulation requirements for 2-step RACH

## Slide 3: Agreements from the first round discussion(1)
TO Compensation is assumed when specifying BS demodulation requirements for 2-step RACH for WA and MR BS. For LA BS, FFS whether T0 compensation is assumed (examing impact of T0 compensation first)
Excluding 0µs TO
Using “4-step RA type” and “2-step RA type” aligned with RRM session and RAN2 for the discussion and specs texts if necessary

## Slide 4: Agreements from the first round discussion(2)
The following setup acceptable for specifying BS demodulation requirements for 2-step RACH:
  Not limiting preamble format
  No re-transmission assumed
  Not specify power offset between preamble and PUSCH/MsgA in the specification and allow TE vendor to decide it during the test with always correct preamble decoding
  1T2R
  TDLC300-100 for FR1, TDLA30-300 for FR2
  SNR on PUSCH/MsgA
  SCS: 15k and 30k for FR1, 60k and 120k for FR2, but only one SCS can be tested
  DMRS configuration 1+1+1 or 1+1 based on evaluation results.
  TB size 56-72 bits, subject to changes with the selection of MCS, PRB number and symbol number, assuming the least padding bits
  Consider MCS level, PRB number and symbol number together, and start with MCS1, 2 PRBs and 14 symbols for FR1, MCS 3, 2 PRBs and 10 symbols for FR2, but leaving other options open

## Slide 5: Way forward (1) – Requirements for LA BS
Whether or not to specify BS demodulation requirements for 2-step RACH for LA BS
  Option 1: No requirements for LA BS
  Option 2: Specify requirements for LA BS with TO = 0.13 µs for FR1 and 0.07 µs for FR2
  Option 3: Cycling values for LA BS, FFS cycling values
  Option 4: Other options not precluded

## Slide 6: Way forward (2)
Whether or not to introduce cycling TO values for specifying 2-step RACH BS demodulation requirements:
  Option 1: No, only introduce specific TO values (non-cycling)
  Option 2: Yes, introducing cycling TO values configuration

## Slide 7: Way forward (3)
Whether or not to introduce TO value(s) larger than CP duration for specifying 2-step RACH BS demodulation requirements
  Option 1: Yes
  Option 2: No

## Slide 8: Way forward (4)
Whether to create 1 or 2 thresholds for TO with declaration of whether TO above the threshold is supported
  Option 1: Yes
    Option 1a: set threshold to CP duration if WF-3 agreed.
  Option 2: No

## Slide 9: Way forward (5)
If cycling values are agreed for TO, what are cycling values for WA/MR BS? (Pending on the agreement on WF-2)
  Option 1: Cycling of {0.1, 0.2, 0.3, 0.4, 0.5, 0.6, 0.7, 0.8, 0.9}µs as in clause 8.4.1.4.2 of 38.141
  Option 2: Cycling of {-X, …-0.1, 0, 0.1, 0.2, 0.3, …, Y}µs, FFS X and Y
  Option 3: Other cycling options not precluded

## Slide 10: Way forward (6)
If cycling values are agreed for TO, what are cycling values for LA BS? (Pending on the agreement on WF-1 and WF-2)
  Option 1: Cycling of {0.1, 0.2, 0.3, 0.4, 0.5, 0.6, 0.7, 0.8, 0.9}µs as in clause 8.4.1.4.2 of 38.141
  Option 2: Cycling of {-X, …-0.1, 0, 0.1, 0.2, 0.3, …, Y}µs, FFS X and Y
  Option 3: Other cycling options not precluded

## Slide 11: Way forward (7)
If Non-cycling values are agreed for TO, what are values for WA/MR BS? (Pending on the agreement on WF-2)
  Option 1:
  Option 2:
  Option 3:

## Slide 12: Simulation setup
Parameter | Values for FR1 | Values for FR2
Preamble format | Free choice | 
Waveform | CP-OFDM | 
Power offset between preamble and MsgA | Free choice | 
Subcarrier spacing for PUSCH | 15kHz, 30kHz | 60kHz, 120 kHz
PUSCH Mapping Type | Option 1: Type A and Type B Option 2: Type A | Option 1: Type A and Type B Option 2: Type A
MCS level | 1 | 3
Number of symbols | 14 | 10
Number of PRBs | 2 | 2
TBS | 56 - 72 bits | 
DMRS | Option 1: 1+1+1 Option 2: 1+1 | Option 1: 1+1+1 Option 2: 1+1
Antenna configuration | 1T2R | 1T2R
Propagation channel | TDLC300-100 | TDLA30-300
TO values | Option 1: Non-cyclic values Option 2: Cyclic values (To be updated) | Option 1: Non-cyclic values Option 2: Cyclic values (To be updated)
Test metric (BLER of MsgA when preambles are correctly detected) | - Option 1: 0.01 - Option 2: 0.1 | - Option 1: 0.01 - Option 2: 0.1
Re-transmission | No retransmission considered |