## Slide 1: Way Forward on Rel-15 Maintenance for Signaling Characteristics
Apple, …
3GPP TSG-RAN WG4 #95-e Meeting R4-2008527
Electronic Meeting, 25 May – 5 June 2020

## Slide 2: FR2 Intra-band CA
Issue 5-1: Assumptions on SSB pattern for FR2 Intra-band CA
  Proposal: For FR2 SCell activation where there is active serving cell in the band, the requirements apply provided that the SSB pattern is same for the active serving cell and the SCell being activated.
Agreement: Agree on the proposed change below
  For FR2 SCell activation where there is active serving cell(s) in the band, the requirements apply provided that the SSB pattern is same for the active serving cell(s) and the SCell being activated

## Slide 3: UE Behavior during MAC CE based TCI State Switch
Issue 5-2-1: Remove the extra term TOk*(Tfirst-SSB) for receiving on the old state
  Agreement : The UE shall be able to receive PDCCH with the old TCI state until slot n + THARQ + 3*Nslotsubframe,u.
    FFS on additional clarification: The UE is not required to receive with old or target TCI state from slot n+ + THARQ + 3*Nslotsubframe,u +1 until the end of the switching delay.

## Slide 4: UE TX/RX During RRC Based TCI State Switch
Issue 5-2-2: UE Tx and RX restriction during RRC based TCI state switch
  Option 1 : UE is not required to receive PDCCH/PDSCH/CSI-RS or transmit PUCCH/PUSCH from slot n + THARQ + 1 until the end of switching period.
  Option 1a we can clarify in the current spec that UE is allowed to transmit HARQ during total switching delay time.
  Option 2: no change

## Slide 5: UE TX/RX During RRC Based BWP Switch
Issue 5-3: UE behaviour for transmission or reception for BWP switching requirements
  Proposal 1: Revise the UE behaviour in current RRC based BWP switching requirement as:
    The UE is not required to transmit UL signals or receive DL signals from slot n+THARQ+1 until the end of switching delay. Where THARQ is the timing between DL data transmission and acknowledgement as specified in TS 38.213 [3].
  Proposal 2: RAN4 to define the duration within which UE is not required to transmit or receive signals for UE specific CBW change in R16.
Option 1: Agree on proposal 1 and proposal 2.
Option 1a: Agree on proposal 1. Agree on proposal 2 for Rel-16.
Option 2 : No change needed.

## Slide 6: Scell deactivation interruption issue for FFS
Issue 5-4 – Further discussion on CR R4-2007661
  FFS: Whether and how RAN4 would specify the starting point and ending point of interruption range for SCell deactivation.