## Slide 1: WF on IAB-MT unwanted emissions
Nokia, Nokia Shanghai Bell
R4-2008784
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: Contributions in RAN4#95-e
R4-2006800, Samsung
R4-2007130, Qualcomm Incorporated
R4-2007576, Ericsson
R4-2007909, Huawei
R4-2007403, ZTE corporation
R4-2007120, Nokia, Nokia Shanghai Bell

## Slide 3: Way forward on FR1 IAB-MT relative ACLR
IAB-MT ACLR minimum requirement in FR1 is 45 dBc
    Samsung: For WA IABMT it may be reasonable to put 45dB here. But according to our simualtion result on Layout 1 scenario 1 based on IAB with assumption based on Micro scenario the ACLR of 30dB is OK to meet 5% throughput loss criteria for co-existence study. We also notice there is further simulation provided recently.Definitly, with 45dBc ACLR for IAB-MT the thoughtput absolute level should be better than the case of 30dB ACLR. However, it is organized and compared in throughput loss way.
    Nokia: Samsung results in R4-1911394 show -13.27 % Tput degradation for cell edge user with 30 dB ACLR. Therefore it is unclear how the comment above is based on simulation results.

## Slide 4: Way forward on OBUE and SEM
For FR2:
  Wide Area IAB-MT shall meet wide area BS OBUE requirements
    Pending agreements on feature level discussion of IAB-MT transmission in DL timeslot, it can be further discussed if in addition, when IAB-MT is configured to transmit in DL timeslot, wide area IAB-MT needs to meet the OBUE requirements of IAB-DU of the same IAB-Node
  Samsung: This should be considered further if this can be applied for out-of-band IAB case. And also we would like understand the scenario and restriction further.
  FFS for local area IAB-MT
      Qualcomm: our proposal is to have these requirements based on the UE specs. what would the problem with that be?
For FR1
  Pending relative ACLR is agreed as 45 dBc, Wide Area IAB-MT shall meet wide area BS OBUE requirements
    Pending agreements on feature level discussion of IAB-MT transmission in DL timeslot, it can be further discussed if in addition, when IAB-MT is configured to transmit in DL timeslot, wide area IAB-MT needs to meet the OBUE requirements of IAB-DU of the same IAB-Node
  FFS for local area IAB-MT
For both FR1 and FR2 the boundary between in-band and spurious region will follow BS requirements.
  Samsung: For BS and IAB DU it will have supported frequency range within supported operating band. Then what is the assumption for IAB-MT?

## Slide 5: Way forward on absolute ACLR
Absolute ACLR to be discussed further in future meetings.

## Slide 6: Way forward on spurious emissions
Spurious emissions are regulatory requirements. Being a network node, IAB-MT shall meet the same spurious emissions requirements as base stations.
  Both category A and category B spurious emissions shall be specified for IAB-MT
  Qualcomm: is there a technical reason or a regulatory one to say that this is a network node and should meet BS requirements? This seems more of a phylosophical problem. the IAB-MT has the functionality of a UE and is also transmitting more like a UE(transmission is scheduled, it can transmit different number of RBs, etc). From this point of view, it seems to be more like a UE than a base station
  Nokia: You can find some discussion on under which ITU definition IAB would fall in R4-1914218 (document and relevant proposal noted). Meeting BS requirement may be needed for SDM forward compatibility.