## Slide 1: WF on simultaneous Rx/Tx for DC_42_n79
Agenda item: 7.19.3
Source: Huawei, HiSilicon, [Skyworks Solutions Inc.]
3GPP TSG-RAN WG4 Meeting # 97-e R4-2016841
Electronic Meeting, Nov 2nd – 13th, 2020

## Slide 2: Background
Based on the contribution [1], there is an ambiguity in the spec about whether DC_42_n79 supports simultaneous Tx/Rx.
In this meeting, companies provided MSD analysis[2] and CR[3] to further discuss this topic.
  UE is implemented with a band n77 filter: simultaneous Tx/Rx cannot be supported
  UE is implemented with a dedicated band n78 or B42 filter simultaneous TX/Rx can be supported with MSD

## Slide 3: 1st round discussion
Based on the 1st round discussion, there are two opinions for DC_42_n79.
  Option 1:
    In Rel-15, the minimum requirements apply only when there is non-simultaneous Tx/Rx operation between E-UTRA and NR carriers for DC_42_n79.
    From Rel-16, simultaneous Rx/Tx capability does not apply for UEs supporting band 42 with a n77 implementation for DC_42_n79 and simultaneous Rx/Tx is optional for DC_42_n79 with the other implementation.
  Option 2:
    From Rel-15, simultaneous Rx/Tx capability does not apply for UEs supporting band 42 with a n77 implementation for DC_42_n79 and simultaneous Rx/Tx is optional for DC_42_n79 with the other implementation.

## Slide 4: WF
If the option 1 is accepted by RAN4, there is no need to specify the MSD for DC_42_n79 in Rel-15. However, the MSD due to cross band isolation for DC_42_n79 shall be specified from Rel-16.
If the option 2 is accepted by RAN4, the MSD due to cross band isolation for DC_42_n79 shall be specified from Rel-15.
To introduce 2.8dB MSD value for victim band 42 with UL aggressor band n79.
The revision of CR R4-2016238 can be implemented based on option 2 and 2.8dB.

## Slide 5: Reference
[1] R4-2011460, CR to 38.101-3 - Correction DC_42_n79 simultaneous Tx/Rx operation, Skyworks Solutions Inc.
[2] R4-2015555, Discussion on asynchronous for DC_42_n79, Huawei, HiSilicon
[3] R4-2016238, CR 38101-3 R15 Band 10 protection and DC_42_n79, Skyworks Solutions Inc.