## Slide 1: WF on 35MHz 45MHz REFSENS AMPR
Qualcomm, Skyworks, […]
­­­3GPP TSG-RAN WG4 Meeting # 97-e R4-2016864
Electronic Meeting, 2nd – 13th Nov., 2020

## Slide 2: Background
Various companies brought contributions for AMPR and REFSENS for 35MHz and 45MHz channel bandwidths
Agreements can be made for n3 35MHz and 45MHz
Agreements can be made for n25 35MHz
No agreements made for 35MHz for n8, n71 and 45MHz for n2 due to large BW
Various issues were brought up using the large BW

## Slide 3: Issues associated with n8, n25, n71 35, 45 MHz
REFSENS degradation due to IM3 of TX image and TX signal or IM3 ACLR overlap
  n8 35M, n71 35M, and n25 45M
  As much as 25-30dB MSD
LB-LB ENDC combination issues
  DC_20A_n8A, DC_13A_n71A, and any future LB-LB combinations have CIM5 issue
Coexistence Issues
  Cases are n71 -> B29/B12
  RB restriction or 12-14dBAMPR required with new NS flag for n71 -> B29 coexistence.
Difficult to assess large relative channel BW impact
  Option 1: ∆MPR not conclusive
  Option 2: ∆MPR = 1dB

## Slide 4: 35MHz and 45MHz REFSENS Agreement
Comparison
No agreement on UL configuration for n8, n71 for 35MHz BW
Large variation of MSD and UL configuration for n8, n71 35MHz
UL configuration was chosen in [1] by keeping the T-R offset / UL allocation ratio the same as the ratio from the next lowest supported UL BW
  Other methods not precluded.
Potential Agreement for UL configuration for n3 and n25 35MHz BW and n3 45MHz BW – To be confirmed next meeting.
REFSENS |  |  |  |  |  | 
Company | n3 |  | n25 |  | n8 | n71
 | 35M | 45M | 35M | 45M | 35M | 35M
QCOM | -85.2 | -80.2 | -81.7 | -68.9 | -69 | -69
SWKS |  |  |  |  | -66.3 | -66.3
MURATA | -86 | -84.2 | -85.4 | -70.7 | -62.2 | -67.6
AAPL |  |  |  |  | -62.3 | -62.5
MTK |  |  |  |  | -69.2 | -70.5
UL Config. 15K |  |  |  |  |  | 
Company | n3 |  | n25 |  | n8 | n71
 | 35M | 45M | 35M | 45M | 35M | 35M
QCOM | [50] | [50] | 45 [40] | 40 | 16 | 16
SWKS |  |  |  |  | 25 | 25
MURATA | [50] | [50] | [40] | 40 | 20 | 20
AAPL |  |  |  |  | 8 | 8
MTK |  |  |  |  | 20 | 20

## Slide 5: n7 35 MHz A-MPR Agreement
Potential agreement using inputs from Skyworks, Apple and Qualcomm
Skyworks/ Apple
Qualcomm
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
35 MHz | 2517.5 ≤ FC ≤ 2552.5 | ≥0, <[2.7 or 3.42] | >0 | A4
 |  | ≥[2.7 or 3.42], <[15.84] | >max (0, 12*SCS*RBend –[3.06]) | A5
 |  | ≥[15.84], <[22.68] | >[12.6] | A6
 |  | ≥[22.68], <[28.8] | >[9.36] | A7
 |  | ≥[28.8] | >0 | A8
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
35 MHz | 2517.5 ≤ FC ≤ 2552.5 | ≥0, <2.7 | >0 | A4
 |  | ≥2.7, <13.5 | >max (0, 12*SCS*RBend –2.7) | A5
 |  | ≥13.5, <23.76 | >9.0 | A6
 |  | ≥23.76, <29.52 | >9.0 | A7
 |  | ≥29.52 | >0 | A8
Potential Agreement
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
35 MHz | 2517.5 ≤ FC ≤ 2552.5 | ≥0, <[3.42] | >0 | A4
 |  | ≥3.42], <[15.84] | >max (0, 12*SCS*RBend –[3.06]) | A5
 |  | ≥[15.84], <[22.68] | >[12.6] | A6
 |  | ≥[22.68], <[28.8] | >[9.0] | A7
 |  | ≥[28.8] | >0 | A8

## Slide 6: n25 and n66 NS_03 A-MPR Agreement
Tentative agreements
  Agree on the updated NS_03 requirement for 35MHz and 45MHz
  Agree to use same NS_03 AMPR for 35MHz and 45MHz as specified in TS38.101-1
Confirm adoption of equation-based proposal in WF for 35/45MHz requirements (R4-2016863).
ΔfOOB MHz | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  |  |  |  |  |  |  |  | Measurement bandwidth
 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 
± 0-1 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 % of channel BW
± 1-6 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 6-10 | -25 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 10-15 |  | -25 | -13 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 15-20 |  |  | -25 | -13 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 20-25 |  |  |  | -25 | -13 | -13 | -13 | -13 | -13 | 1 MHz
± 25-30 |  |  |  |  | -25 | -13 | -13 | -13 | -13 | 1 MHz
± 30-35 |  |  |  |  |  | -25 | -13 | -13 | -13 | 1 MHz
± 35-40 |  |  |  |  |  |  | -25 | -13 | -13 | 1 MHz
± 40-45 |  |  |  |  |  |  |  | -25 | -13 | 1 MHz
± 45-50 |  |  |  |  |  |  |  |  | -25 | 1 MHz

## Slide 7: WF
Due to the issues mentioned with 35MHz for Low bands and 45MHz with n2, the following WF is considered:
Consider asymmetric UL/DL for n8, n71, n25
  Keep 35MHz for n8, n71 on the DL
  Keep 45MHz for n25 on the DL
  Configuration table is already in place
  Possibly introduce BCS1 for affected bands
Re-evaluate REFSENS for the following with agreed UL configuration
  20MHz UL/35MHz DL for n8 (Skyworks has provided)
  20MHz UL/35MHz DL for n71 (Skyworks has provided)
  45MHz DL only for n25 with UL restricted to ≤ 40MHz
  35MHz UL/35MHz DL, 45MHz UL/45MHz DL for n3 (Qualcomm, Murata has provided)
  35MHz UL/35MHz DL for n25 (Qualcomm, Murata has provided)
Channel location(s) of asymmetric UL (Worst Case/Best Case) DL cases can be studied for MSD test points
Potential agreement for UL configuration on slide 4 to be confirmed next meeting.
Assume UL RB allocation is closest to DL band
DL band is fully allocated.
Other companies encouraged to bring measurements and analysis

## Slide 8: References
R4-2016600, “35M_45M AMPR, MPR, REFSENS”, Qualcomm Incorporated, 3GPP TSG-RAN WG4 #97-e, revised from R4-201473
R4-2015432, “REFSENS of n3, n8, n25 and n71 for new channel bandwidth”, Murata Manufacturing Co Ltd., 3GPP TSG-RAN WG4 Meeting # 97-e
R4-2015800, “Specification impact of additional 35&45MHz channel bandwidths”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016010, “n71 35MHz AMPR and MSD Measurements”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016011, “n8 35MHz AMPR and MSD Measurements”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016027, “n7 35MHz AMPR and MSD Measurements”, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 #97-e
R4-2016060, “Introduction of 35MHz and 45MHz regarding CA, DC, V2x combinations”, Ericsson, 3GPP TSG-RAN WG4 #97-e
R4-2016295, “Introduction of 35 MHz for n8, n66, n71 and 45 MHz for n66”, Apple Inc., 3GPP TSG-RAN WG4 #97-e
R4-2014186, “REFSENS of n8 and n71 for 35MHz channel bandwidth”, MediaTek Inc., 3GPP TSG-RAN WG4 #97-e
R4-2014911, “UE RF requirements tables with channel BW dependency”, Apple Inc., 3GPP TSG-RAN WG4 #97-e