## Slide 1: WF on BS MU/TT for n262
Nokia, Nokia Shanghai Bell, Ericsson
3GPP TSG-WG RAN4 Meeting #97-e
Electronic meeting, 2nd – 13th November, 2020
R4-2016881

## Slide 2: Background
During RAN4#97-e, the following documents on n262 BS MU/TT have been submitted:
  R4-2016191; TP to TR 38.847: BS RF requirements; Nokia, Nokia Shanghai Bell
  R4-2016155; 47GHz band TT for NR BS RF requirement; Keysight Technologies UK Ltd
  R4-2016971; Email discussion summary for [97e][130] NR_47GHz_Band

## Slide 3: WF on Tx MU
During the first round of RAN4#97-e, estimated MU for 47.2-48.2GHz range was discussed as summarized in the table below
It is proposed to agree on Estimated MU values in the last column, numbers in [] need to be confirmed during RAN4#98-e.
Tx test | TS 38.141-2 24.25 ~ 29.5GHz | TS 38.141-2 37 ~ 43.5GHz | Estimated MU 47.2~48.2GHz Keysight R4-2016155 | Estimated MU 47.2~48.2GHz Nokia R4-2016191 | Ericsson | Huawei | Proposed MU
EIRP | 1.7 | 2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2
EIRP extreme | 3.1 | 3.3 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5
Output Power | 2.1 | 2.4 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6
Tx Off power | 2.9 | 3.3 | 3.6 | 3.5 | 3.5 | 3.6 | [3.5-3.6]
Relative ACLR | 2.3 | 2.6 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8
Absolute ACLR | 2.7 | 2.7 | 2.9 | 2.7 | 2.7 | 2.9 | [2.7-2.9]
OBUE (close) | 2.7 | 2.7 | 2.9 | 2.7 | 2.7 | 2.9 | [2.7-2.9]

## Slide 4: WF on Rx MU
During the first round of RAN4#97-e, estimated MU for 47.2-48.2GHz range was discussed as summarized in the table below
It is proposed to agree on Estimated MU values during RAN4#98-e.
Rx test | TS 38.141-2 24.25 ~ 29.5GHz | TS 38.141-2 37 ~ 43.5GHz | Estimated MU 47.2~48.2GHz Nokia R4-2016191
Reference sensitivity | 2.4 | 2.4 | 2.4
ACS | 3.4 | 3.4 | 3.4
IBB | 3.4 | 3.4 | 3.4
Rx IM | 3.9 | 3.9 | 3.9
In-channel selectivity | 3.4 | 3.4 | 3.4

## Slide 5: Thank you