## Slide 1: WF on SSB-less SCell activation delay requirement
Qualcomm Inc.
3GPP TSG-RAN4 Meeting #97-e
Electronic Meeting, Nov 2 – 13, 2020
Agenda item: 4.7
R4-2017035
Document for: Discussion

## Slide 2: Background
UE supporting feature 1-10 “scellWithoutSSB ” is able to use SS/PBCH block from other Cells for time/frequency synchronization of SCell without SS/PBCH block
SSB-less SCell activation delay requirement for deactivated FR1 SCell is not defined in the current version 38.133 spec, whereas FR2 SCell activation requirements include SSB-less SCell activation latency.
QCL association across CCs can be established by a field of ‘cell’ in QCL-Info of TCI-Sate
  (TS38.331) The RS can be located on a serving cell other than the serving cell in which the TCI-State is configured only if the qcl-Type is configured as typeC or typeD. See TS 38.214 [19] clause 5.1.5.

## Slide 3: Proposal
RAN4 to define SSB-less FR1 SCell activation delay requirement as follows:
  If the SCell being activated belongs to FR1 and if there is at least one active serving cell contiguous to the Scell on that FR1 band, if the UE [supporting scellWithoutSSB] is not provided with any SMTC for the target SCell, Tactivation_time is 3 ms[, provided
    the RS (s) of SCell being activated is (are) QCL-TypeA with TRS (s) of the SCell being activated and the TRS (s) is (are) QCL-TypeC with SSB (s) of one active serving cell on that FR1 band.]
  FFS on non-contiguous intra-band CA