## Slide 1: WF on NR V2X RRM requirements
LG Electronics
3GPP TSG-RAN WG4 #97e
Electronic Meeting, 2-13 Nov., 2020
R4-2017100

## Slide 2
WF on Core maintenance
Interruption to WAN for switching between LTE SL and NR SL
  Define interruption requirement regarding that RAN4 does not consider generally a specific UE RF architecture but considers different UE RF architectures.
Whether to define interruption requirement on LTE SL due to NR SL sync source is changed
  Define interruption requirement regarding that as long as subframe/slot boundaries have to be aligned, whenever there is a sync source change, regardless of implementation, timing can be changed

## Slide 3
WF on Performance
Absolute accuracy of L1 SL-RSRP measurement
  Define ±4.5dB as absolute measurement accuracy of L1 SL-RSRP at SNR=0dB when measured at UE antenna connector.
NR V2X operating bands
  Introduce NR_TDD_FR1_B for n38 and NR_TDD_FR1_J for n47 for NR V2X operating bands.
Minimum NR V2X RPs related to side condition
  For NR_TDD_FR1_B
    -126.5 dBm/15kHz , -123.5dBm/30kHz, -120.5dBm/60kHz @ Es/Iot  -6 dB
    -120.5 dBm/15kHz , -117.5dBm/30kHz, -114.5dBm/60kHz @ Es/Iot  0 dB
  For NR_TDD_FR1_J
    -122.5 dBm/15kHz , -119.5dBm/30kHz, -116.5dBm/60kHz @ Es/Iot  -6 dB
    -116.5 dBm/15kHz , -113.5dBm/30kHz, -110.5dBm/60kHz @ Es/Iot  0 dB

## Slide 4
WF on Test Cases
Common resource pool configuration
  Configure one Rx resource pool and one normal Tx resource pool
  Configure subchannel size with 10RB
  Configure Sensing window with 100ms
Test Cases
  Introduce Test for Resource Pre-emption
  Introduce Test for Resource Re-evaluation (a separated test case from pre-emption test)

## Slide 5
WF on Test for Selection / Reselection of V2X Synchronization Reference Source
Test set-up for GNSS
  Set up with 3 SyncRef UEs
    SyncRef UE1 (sync to gNB directly), SyncRef UE2 (sync to GNSS in-directly) and SyncRef UE3 (sync to GNSS directly).

## Slide 6
WF on PSCCH RMC
  Table A.3.19.3-1: PSCCH Reference Measurement Channels
Parameter |  | Unit | Value
Reference channel |  |  | CC.1A HD
Channel bandwidth |  | MHz | Note2
Number of PSCCH symbols per slot |  |  | 2
Number of PSCCH RB |  |  | 10
Modulation |  |  | QPSK
Information Bit Payload (without CRC) |  | Bits | [28] 26
Information Bit | Number of DMRS ports |  | 0 (1 port)
 | Priority |  | As set by higher layers
 | Resource reservation period |  | N/A
 | Modulation and coding scheme |  | Set as the PSSCH MCS specified in the test
 | DMRS pattern |  | 0 (2 DMRS)
 | 2nd stage SCI format |  | 0 (Multi-cast)
 | Beta offset indicator |  | Set as specified in the test
 | Frequency resource assignment |  | Set as per PSSCH RB allocation specific in the test
 | Time resource assignment |  | Set as per PSSCH slot allocation specific in the test
 | Reserved bits |  | Set all these bits to 0
Transport block CRC |  | Bits | 24
Binary Channel Bits (see Note 1) |  | Bits | [172] 360
Note 1: Binary channel bits calculated under assumption of 2 CP-OFDM symbols per subframeslot Note 2: Channel bandwidth depends on test configuration |  |  | 

## Slide 7
WF on PSSCH RMC
  Table A.3.19.3-2: PSSCH Reference Measurement Channels
Parameter | Unit | Value
Reference channel |  | CD.1A HD
Sidelink transmission mode |  | 2
Channel bandwidth | MHz | Note1
Allocated PSSCH resource blocks |  | 10
Number of PSSCH symbols per slot |  | 10
Modulation |  | QPSK
Target Code Rate |  | 1/3
Information Bit Payload (Transport block size) | Bits | [576] 672
Transport block CRC | Bits | 24
Number of PSSCH HARQ retransmissions |  | 0
Binary Channel Bits | Bits | [1920 ] 2160
Note 1: Channel bandwidth depends on test configuration Note 2 : 2nd state SCI and PSFCH are not allocated per slot. |  |