## Slide 1: WF on R16 NR RRM enhancements - BWP switching on multiple CCs, UL spatial info switch
Intel Corporation
3GPP TSG-RAN WG4 Meeting #97-e R4-2017362
Electronic Meeting, 2-13, Nov. , 2020

## Slide 2: Simultaneous BWP switching on multiple CCs in core part(1)
Scenario for simultaneous RRC based BWP switch on multiple CCs
  Wait for conclusions in [201]
Clarification for Non-simultaneous RRC based BWP switch on multiple CCs
  Clarify that N and M are the number of CCs in the first CG and in the second CG respectively for RRC based non-simultaneous BWP switching on multiple CCs. M=1 if the BWP switch is performed on single CC.

## Slide 3: Simultaneous BWP switching on multiple CCs in core part (2)
Whether to define new UE capability- Parallel processing of BWP switching in different frequency ranges
Agreement in GTW session.
    Remove the feature

## Slide 4: UL Spatial Relation Info Switching requirement in core part
Define requirements for the case when the UL signal has spatial relation to an unknown DL RS
Agreement in GTW session.
  For MAC-CE based: THARQ + 3ms + TL1-RSRP.
  For RRC based: TRRC-processing + TL1-RSRP
  Do not define any test cases for this scenario

## Slide 5: Simultaneous BWP switching on multiple CCs test case design(1)
Agreement in 1st round discussion
Number of CCs undergoing multiple BWP switching
  Agreement: 2
Test duplication for EN-DC and SA
  Agreement: Duplicated. Further discuss about applicable rule
Interruption test is needed or not
  Agreement: Test interruption requirements along with delay requirements in one test
Cell configuration with or w/o interruption test
  Agreement: for EN-DC, LTE PCell + NR PSCell + NR SCell
Whether DCI+Timer based simultaneous BWP switch switching can be applied in one test
  Agreement: Both DCI+Timer based BWP switch can be tested in one testcase
Whether define test for Cross-carrier scheduling based Simultaneous BWP switching
  Agreement: Only define self-scheduling based test cases in NR_RRM_enh.

## Slide 6: Simultaneous BWP switching on multiple CCs test case design(2)
CC combinations for BWP switch
Agreement in GTW session:
Define test cases for
  FR1+FR1 simultaneous BWP switch
  FR2+FR2 simultaneous BWP switch
  FFS: FR1+FR2 simultaneous BWP switch
  FFS: FR1+FR2 non-simultaneous BWP switch
Note 1: the agreement applies for DCI/Timer based switching. For RRC based switching further discussion shall take place whether it is feasible to have simultaneous BWP switch.
Note 2: Feasibility of FR1+FR2 testing shall be addressed

## Slide 7: Simultaneous BWP switching on multiple CCs test case design(3)
Simultaneous case or simultaneous + partial
Sub1: For RRC based BWP switching
  Postpone defining testcases with RRC based simultaneous BWP switch and clarify the scenario first.
Sub2: DCI/Timer based BWP switching:
- FFS:
  Option 1:
    Only define simultaneous multiple BWP switch test cases
  Option 2:
    Define both simultaneous and non-simultaneous multiple BWP switch test cases

## Slide 8: Simultaneous BWP switching on multiple CCs test case design(4)
Cell configuration with or w/o interruption test
  For SA case:
    NR PCell + 2 NR Scells
Numerology difference b/w cells and/or BWPs in same FR
  same SCS configuration among all involved CCs in the same FR.

## Slide 9: Simultaneous BWP switching on multiple CCs test case list
DCI/Timer based simultaneous BWP switch test case list
  TC1: DCI-based and Timer-based simultaneous Active BWP Switch on multiple CCs on FR1 in EN-DC (LTE PCell+ NR FR1 PSCell+ NR FR1 SCell )
  TC2: DCI-based and Timer-based simultaneous Active BWP Switch on multiple CCs on FR2 in EN-DC (LTE PCell+ NR FR2 PSCell+ NR FR2 SCell )
  TC3: DCI-based and Timer-based simultaneous Active BWP Switch on multiple CCs on FR1 in SA (NR FR1 PCell+ NR FR1 SCell + NR FR1 SCell)
  TC4: DCI-based and Timer-based simultaneous Active BWP Switch on multiple CCs on FR2 in SA (NR FR1 PCell+ NR FR2 SCell + NR FR2 SCell)
- FFS:
  FR1+FR2 simultaneous BWP switch
DCI/Timer based non-simultaneous BWP switch test case
  FFS
  RRC based simultaneous/non-simultaneous BWP switch test case
  FFS

## Slide 10: UL Spatial Relation Info Switching test case list
Agreement in 1st round discussion
TC1: MAC-CE based spatial relation switch associated with a known DL-RS in EN-DC for PUCCH
TC2: RRC based spatial relation switch associated with a known DL-RS in EN-DC for periodic SRS
TC3: MAC-CE based spatial relation switch associated with a known DL-RS in SA for PUCCH
TC4: RRC based spatial relation switch associated with a known DL-RS in SA for periodic SRS