## Slide 1: WF on test cases for IAB-MTs
ZTE Corporation
3GPP TSG-RAN WG4 #97-e
Electronic Meeting, 2-13 Nov., 2020
R4-2017383

## Slide 2: Way Forward - Test cases
Only RRM performance requirements for IAB-MT are needed and the IAB-MT shall be tested with DU part disabled.
Use conducted testing for IAB type 1-H and OTA testing for IAB type 2-O.
RRM tests for IAB type 1-O are not to be defined.

## Slide 3: Way Forward - Test cases
Define test cases for RRM requirements under NR SA.
Take UE test cases in TS 38.133 Annex as baseline when defining test cases for IAB-MTs.
The performance requirements shall be differentiated between wide area IAB-MT and local area IAB-MT if needed.

## Slide 4: Way Forward - Scope of test cases
For RRC Re-establishment, only unknown target cell should be considered in the testing and only local-area IAB-MT to be tested.
Don’t define separate test cases of random access for IAB-MT.

## Slide 5: Way Forward - Scope of test cases
RRM tests are defined in both FR1 and FR2 to verify all IAB-MT requirements defined in TS 38.174.
RRM tests are defined in FR1 for IAB type 1-H and FR2 for IAB type 2-O to verify all IAB-MT requirements defined in TS 38.174 that are also feasible to test.

## Slide 6: Way Forward - Responsibility
The RRM performance testing requirements shall be defined and maintained in RAN4, and no RAN5 work to be involved.

## Slide 7: Way Forward - Responsibility
Define IAB-MT RRM performance requirements.
  The requirements will be captured in TS 38.174
Don't define IAB-MT RRM conformance tests.

## Slide 8: Way Forward - Work Split
FFS study the following options:
Option 1: Only split for different features
Option 2: Split at a detailed level

## Slide 9: Way Forward - Core Maintenance
FFS Whether to specify applicable MGs for local area IAB-MTs
Options:
  Option 1: Remove gap aspects from requirements in 38.174
  Option 2: Define at least one gap pattern for local area IAB-MT
  Other options not precluded