## Slide 1: WF on UE demodulation and CSI reporting requirements for FR2 DL 256QAM
China Telecom
3GPP TSG-RAN4 Meeting #97e
Electronic Meeting, 2-13 Nov., 2020
Agenda item: 7.10.1
R4-2017536
Document for: Approval

## Slide 2: Background: WFs in previous meetings
RAN4 #94e-Bis
  WF: R4-2005531
RAN4 #95e
  WF: R4-2008817
  RAN4 #96e
  WF: R4-2012666

## Slide 3: PDSCH Demodulation: Main Parameters
  Propagation condition
  Introduce test case with TDLD30-75 based on the assumption that we can complete the work for introducing TDL-D channel model into specification in RAN4#98e. If no conclusion for introducing TDL-D channel model in RAN4#98e, then RAN4 will adopt TDLA30-300 instead of TDLD30-75.
  In RAN4#98e, companies provide simulation results (including 70%TP ideal and impairment SNR points and TP curves) in the template provided by Intel.

## Slide 4: PDSCH Demodulation: Main Parameters
  Specification of TDLD30 channel model into TS38.101-4
  Option 1: derived using only Steps 1-5 from methodology in Section B.2.1 of TS 38.101-4 for Rayleigh components
  Option 2:
  Companies are encouraged to check if the above option 1 is agreeable and provide feedback in RAN4 draft reflector during 16th - 27th Nov after the meeting.
Tap # | Delay | Power in [dB] | Fading distribution
1 | 0 | -0.2 | LOS path
 | 0 | -12.4 | Rayleigh
2 | 20 | -21 | Rayleigh
3 | 40 | -16.7 | Rayleigh
4 | 55 | -18.3 | Rayleigh
5 | 80 | -21.9 | Rayleigh
6 | 120 | -27.8 | Rayleigh
7 | 240 | -23.6 | Rayleigh
8 | 285 | -24.8 | Rayleigh
9 | 290 | -30.0 | Rayleigh
10 | 375 | -27.7 | Rayleigh
Tap # | Delay | Power in [dB] | Fading distribution
1 | 0 | -0.2 | LOS path
 | 0 | -13.5 | Rayleigh
2 | 2 | -18.8 | Rayleigh
3 | 18 | -21 | Rayleigh
4 | 40 | -22.8 | Rayleigh
5 | 42 | -17.9 | Rayleigh
6 | 54 | -18.3 | Rayleigh
7 | 78 | -21.9 | Rayleigh
8 | 122 | -27.8 | Rayleigh
9 | 238 | -23.6 | Rayleigh
10 | 282 | -24.8 | Rayleigh
11 | 292 | -30 | Rayleigh
12 | 376 | -27.7 | Rayleigh

## Slide 5: Agreed simulation parameters in previous meetings #1
Parameter | Value
Tx EVM | 3%
Rx impairment modelling and band agnostic requirements | Not explicitly model Rx impairment
SCS | 120 kHz
Channel bandwidth and PRB allocation | 50MHz CBW with full PRB allocation
Rank | Rank 1 only
MCS | MCS 20
TDD Configuration | DDDSU, S=10D:2G:2U
SSB configuration | Periodicity 20 ms, Allocated in first slot within 20ms
PDCCH duration | Symbol #0 in each slot
PDSCH configuration | Full DL slots: Start symbol 1, Duration 13 Special slots: Start symbol 1, Duration 9
PDSCH mapping type | Type A

## Slide 6: Agreed simulation parameters in previous meetings #2
Parameter | Value
PRB bundling size and Precoding model | PRB bundling size: 2 Precoding model: Random Precoding, per slot , WB granularity
DM-RS configuration | Type 1 single symbol front loaded, 1 additional DMRS
PT-RS configuration | per 2PRB in frequency domain per symbol in time domain
TRS configuration | 20 ms periodicity, 2 slots, Offset 10 ms
Overhead for TBS determination | 6
HARQ RV sequence | {0, 2, 3, 1}
HARQ process number | 8
Receiver assumption | MMSE-IRC
MIMO configuration | 2Tx 2Rx ULA low
Test metric | 70% of max TP

## Slide 7: SDR Requirements
Whether to define SDR requirements for FR2 256QAM
  No SDR test cases for FR2 256QAM

## Slide 8: CQI reporting Requirements
Introduce fading CQI test cases only under rank1 with CQI table 2 in FR2
Fading CQI test cases under rank1 transmission with CQI table 2:
  SNR: FFS for higher test points
  Options for further consideration:
    Option 1: 17/18 dB
    Other options are not precluded.
In RAN4#98e, encourage companies to provide simulation results in the template provided by China Telecom
  SNR point:
    Cover at least lower SNR at 6/7 dB, and higher SNR at 16/17/18/19/20/21/22/23/24 dB
  Simulation output:
    Percentage of Reported CQI Index not in {median CQI1 -1, median CQI1 +1}
    BLER with following CQI
    TP ratio with following CQI and Median CQI
    Percentage of reported CQI index > 11
  Finalize the CQI reporting requirements in RAN4 #98e.

## Slide 9: Agreed parameters in previous meetings
  If it is agreed to define FR2 CQI reporting test for CQI table 2,
  Use channel bandwidth of 50MHz and reuse the other parameters in Rel-15 FR2 CQI tests, i.e., parameters in Table 8.2.2.2.2.1-1 in TS38.101-4.
  Consider the following test applicability:
    If UE passes the test with CQI Table 2, then it can skip the corresponding test with CQI Table 1
    Note: Similar to the existing CQI table 1 test, the test for CQI Table 2 will cover both lower SNR and higher SNR.