## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson, Samsung
3GPP TSG-RAN4 Meeting #97e
Electronic Meeting Nov 2nd – Nov 13th, 2020
Agenda item: 7.16.1.2
R4-2017562
Document for: Approval

## Slide 2: Timeline of previous agreements
#92
  WF: R4-1910017
#92bis
  WF: R4-1912834
  simulation assumptions: R4-1912811
#93
  WF: R4-1915858
  Simulation assumptions: R4-1915859
#94e
  WF: R4-2002393
  Simulation assumptions: R4-2002394
#94e-Bis
  WF: R4-2005549
  Simulation assumptions: R4-2005550
#95e
  WF: R4-2008846
  Simulation assumptions: R4-2008847
#96e
  WF: R4-2012762
  Simulation assumptions: R4-2012765

## Slide 3: Simulation assumptions
Detailed simulation assumptions:
  R4-2017563

## Slide 4: Type II test setup
Introduce Rel-15 Type II codebook requirements with SU-MIMO set-up under the condition that with proper test parameters, test metric/ test requirements and test procedure to ensure enough performance difference over than Type I i.e. UE which employ Type I reporting will fail in the test case
Test metric : Further check results based on following candidate options during 2nd round
  Option 1: Following PMI/Random PMI
  Option 2: Following with Type II codebook / following PMI with Type I codebook
Further study and define proper performance requirements if needed under MU-MIMO scenario in Rel-17 performance enhancement WI.

## Slide 5: Parameters for SU-MIMO Type II page 1
Codebook construction
  16Tx ports (N1,N2) = (4,2), (O1, O2) = (4,4)
L (numberOfBeams)
  2
Npsk (phaseAlphabetSize)
  8
SubbandAmplitude
  True
PMI-FormatIndicator
  Subband
Propagation condition
  TDLA30-5
MIMO correlation
  XP Medium as Baseline
  XP (custom) Low only can be considered if XP medium not workable

## Slide 6: Parameters for SU-MIMO Type II page 2
MCS and rank
  MCS 20, rank 2
Beam steering model
  For Rel-15 Type II codebook test:
    Configure only two beams in beam steering model for Rel-15 Type II codebook test.
  specifying beam steering model into specification:
    Reuse the agreement from Rel-16 eMIMO demod.
Subband size
  8 for FDD and 16 for TDD

## Slide 7: Parameters for SU-MIMO Type II page 3
Implementation of Random type II PMI
Tentative agreement:
Use the following as baseline. Other proposals can be considered in the next meeting based on consensus.
  For beam randomization
    Option 2: Limit the set of possible beams to the possible beams under the configuration of following PMI, i.e., set L=2 for random PMI generation
  Amplitude and phase coefficient randomization
    Option 2B: Set the same NPSK, subbandAmplitude with the configuration for follow PMI for random PMI generation.

## Slide 8: Parameters for SU-MIMO Type II page 4
SNR point for type II PMI
  Option 1: SNR point that achieves 90% TP with follow type II PMI (baseline)
  Option 2: SNR point that achieves 70% TP with follow type II PMI
Test metric for type II PMI
  Option 1: TP ratio between following PMI and rand PMI (Agreement in the previous meeting)
  Option 2: TP ratio between type II follow PMI and type I follow PMI

## Slide 9: Simulation Assumption alignment
Beam-Steering Approach
  Enable two independent beam directions applying the beam for comparison both Type II and Type I cookbook simulation

## Slide 10: Test metric for using random PMI reference
Take the test metric with TP ratio of following Type II PMI/random Type II PMI as test metric for Rel-15 Type II codebook requirement if there is performance difference with the following feasibility checking with TP ratio 1a and TP ratio 1b metric as
  TP ratio 1a: following Type II PMI/random Type II PMI
  TP ratio 1b: following Type I PMI/random Type II PMI
Check whether the test metric with following Type II PMI/following Type I is feasible for optional UE features.

## Slide 11: For information
(Custom) Low correlation:
Correlation Model | 1 | 2 |  | γ
Custom correlation | 0.05 | 0.05 | 0.05 | 0.95