## Slide 1: WF on extreme temperature conditions for all applicable FR2 UE RF test cases
vivo
3GPP TSG-RAN WG4 Meeting #97-e R4-2017596
Electronic Meeting, 2-13 Nov., 2020
Agenda item: 13.1
Document for: Approval

## Slide 2
Background
In 38.101-2, some requirements are clearly stated not applicable for ETC testing, including: UE EIRP and EIS spherical coverage, Power control, EVM, and UE beam correspondence, due to 3D scan is not supported under ETC system.
In this enhanced test methods SI, supporting extreme temperature conditions for all applicable FR2 UE RF test cases is the final target.

## Slide 3: Way Forward
  From testing system perspective, the supporting of 3D scan with extreme temperature condition is confirmed by at least one TE vendor.
  RAN4 needs to further quantify and mitigate the impacts due to ETC 3D scan solution, and discuss how to treat some RF requirements applicability restrained to NTC.
  The impacts on requirements, measurement uncertainty and testing time should be quantified in RAN4
    RAN4 to calculate the EIRP shift of each point induced by thermal effect during the 3D scan, and the deviation should be considered as one of the aspects for test tolerance
    Perform simulation to calculate the impacts of temperature on FR2 beamforming, and analyse the performance difference under 3D scan (spherical coverage and TRP) with ETC and NTC
    Identify new MU elements related to ETC testing, and test tolerance of [x] dB is required to address the measurement impact under ETC

## Slide 4: Simulation assumption for ETC
  Details of test methods enhancement need to be further discussed.
  The basic UE assumption in [R4-1902684] for Spherical coverage can be reused for extreme temperature condition simulation to identify the impacts on UE performance
    LNA noise figure, magnitude error, phase shifter, and RSRP error would be aspects can be considered

## Slide 5: Reference
  [1] R4-2016214, “On extreme temperature condition testing”, Keysight, RAN4#97-e, Nov., 2020
  [2] R4-2016223, “Views on FR2 extreme condition testing”, vivo, RAN4#97-e, Nov., 2020
  [3] R4-1902684, “WF on simulation assumptions for BC tolerance requirements”, LG Electronics, RAN4#90, Feb., 2019
  [4] R4-2017429, Email discussion summary for [97e][331] FR2_enhTestMethods, Moderator(Apple)