## Slide 1
WF on testability aspects for the introduction of the new band n262
3GPP TSG-RAN WG4 Meeting #97-e R4-2017599
Electronic Meeting, Nov. 2nd – Nov. 13th, 2020
Agenda Item: 13.1.7
Apple Inc.

## Slide 2: Background
RAN4 discussed the following issues related to testability of band n262:
  Issue 7-1-1: Upper frequency limit
  Issue 7-1-2: Antenna aperture
  Issue 7-1-3: MU
  Issue 7-2-1: Open issues with the RF test setup for applicability of permitted test methods to n262
  Issue 7-2-2: Open issues with the RRM test setup for applicability of permitted test methods to n262
  Issue 7-2-3: Open issues with the demodulation test setup for applicability of permitted test methods to n262
  Issue 7-3-1: Open issues with the applicability of test methodology enhancements to n262

## Slide 3: WF1: Agreements on testability parameters
Upper frequency limit includes the OOB region (i.e. 48.2 + 0.8 = 49 GHz)
According to the RAN4/RAN5 work split, it is assumed RAN5 will continue to develop the detailed MU budget, while RAN4 is responsible for the preliminary assessment of measurement uncertainty, where applicable
Antenna aperture
  Proposals:
    Alt 1-1: Adopt the effective antenna aperture approach, similar to the agreed concept for FR1 RTS test method, for FR2 enhanced test method to reduce the measurement distance. The effective antenna aperture approach should be applied for all the PCs, reasonable assumption of Deff should be defined based on the feedback of OEMs
    Alt 1-2: Define antenna aperture based on a device supporting multiple FR2 bands
  Agreement:
    Further discussion is encouraged to align on this parameter by the next meeting

## Slide 4: WF2: Open issues related to permitted test methods
RF test setup
  Far-field criteria for the DFF system (Clause 5.2.1.2)
  IFF near-field/far-field boundary and path loss (Clause 5.2.3.2)
  Determine which uncertainy elements are impacted by the new frequency range and determine a preliminary assessment of their value
RRM test setup
  Reference point SNR derivation (Clause 6.2.1.4.3)
  Determine which uncertainy elements are impacted by the new frequency range and determine a preliminary assessment of their value
Demodulation test setup
  Reference point SNR derivation (Clause 7.2.1.3.1)
  Determine which uncertainy elements are impacted by the new frequency range and determine a preliminary assessment of their value
All aspects related to the extension of the frequency range of permitted methods should be handled separately from the test methodology enhancement discussions

## Slide 5: WF3: Open issues related to methodology enhancements
The work on methodology enhancements related to Objectives 1 through 6 should be directly integrated into the relevant discussion, such that:
  For all objectives:
    Preliminary assessment of uncertainty is performed up to the agreed upper frequency limit
    All aspects relevant to methodology enhancements for band n262 should be included in the corresponding objective discussion agenda
  For low UL / high DL power test cases:
    The scale of low UL / high DL power testability issues needs to be evaluated
    The analysis of beam management sensitivity, “black box/black & white box” approaches, and potential improvement of permitted test methods up to the agreed upper frequency limit needs to be performed
  For the FR2 CA objective:
    Relevant agreements are already captured by the WF in R4-2017595
  For the ETC objective:
    Study the applicability of the extreme conditions up to the agreed upper frequency limit

## Slide 6: References
Reference | Tdoc | Source | Title
[1] | R4-2014922 | Apple Inc. | Band n262 testability
[2] | R4-2016224 | vivo | Discussion on Testability issue of 47GHz band