## Slide 1
WF on single link tests for NR V2X demodulation performance
3GPP TSG-RAN WG4 Meeting #97-e Electronic Meeting, 2 – 13 Nov., 2020
Agenda Item: 7.3.7.1
R4-2017687
LG Electronics

## Slide 2: Reference receiver
Common assumptions for reference receiver
  CFO estimation: Cross-DMRS symbol CFO estimation.
  CE channel estimation:
    Frequency domain interpolation: MMSE interpolation
    Time domain interpolation: Linear interpolation
  RX window: CP/2 from GNSS

## Slide 3: PSSCH demodulation
Test 1: QPSK for 500km/h relative velocity (already agreed the test)
  20 PRB for PSSCH resource allocation, FFS for Sub-channel size with following options
    Option 1: 10 PRB sub-channel size and number of allocated sub-channels is 2
    Option 2: 20 PRB sub-channel size with 10 RB size for PSCCH
  PSFCH periodicity : keep both option open and encourage companies to bring results for both options in next meeting and planed to make decision in RAN4#98e
    Option 1: 1 periodicity
    Option 2: 4 periodicity
  DMRS pattern
    {3,4} DMRS symbols if PSFCH periodicity is 4
    3 DMRS symbols if PSFCH periodicity is 1
  Propagation condition
    Option 1: TDLA30
    Option 2: TDLB100 or allocation 3symbol for PSCCH
     Option 1 is baseline and companies are encouraged to provide analysis for option 2 (error floor and margin to 10% BLER).
  Beta value for 2nd stage SCI
    Beta value = 3.5 and if technical issue will be observed, beta value can be revised in the next meeting.

## Slide 4: PSSCH demodulation
Additional following test is introduced
  Option 1: [Test 2] 16QAM for 260km/h relative velocity
  Option 2: [Test 3] 64QAM for 30km/h relative velocity
  Option 3: both option 1 and option 2
   Keep FFS for above options and make decision in RAN4#98e

## Slide 5: PSSCH demodulation
Test 2: 16QAM for 260km/h relative velocity
  If the test is introduced, following parameters are considered
  PRB for PSSCH resource allocation
    Option 1: 10 PRB
    Option 2: 20 PRB and FFS for sub-channel size
  PSFCH periodicity
    4 periodicity
  DMRS pattern
    Option 1: {3,4} DMRS symbols if PSFCH periodicity is 4
    Option 2: {2,3} DMRS symbols if PSFCH periodicity is 4
  Beta value for 2nd stage SCI
    Beta value = 5 and if technical issue will be observed, beta value can be revised in the next meeting.

## Slide 6: PSSCH demodulation
Test 3: 64QAM for 30km/h relative velocity
  If the test is introduced, following parameters are considered
  PRB for PSSCH resource allocation
    Option 1: Align with Test 1
    Option 2: 10 PRB
  PSFCH periodicity
    Option 1: 1 periodicity
    Option 2: 4 periodicity
  DMRS pattern
    2 DMRS symbols when PSFCH periodicity is 1 or 4
  Beta value for 2nd stage SCI
    Beta value = 5 and if technical issue will be observed, beta value can be revised in the next meeting.

## Slide 7: PSSCH demodulation
Test for 256QAM modulation order
  Option 1: Define performance requirement
    Applicability rule can be considered if the test is introduced.
  Option 2: Do not define performance requirement
  The final decision will be made in RAN4#98e.
Test for gNB based sync
  Option 1: Define performance requirement with 1300Hz FO and ±24Ts TO
  Option 2: Do not define performance requirement
   The final decision will be made in RAN4#98e.

## Slide 8: PSCCH demodulation
Payload size
  Option 1: 26bit
  Option 2: 24bits
   Depending on decision of sub-channel size, the final decision will be made in RAN4#98e
Relative velocity
  260km/h (TDLA30-1400)
Parameters | Option 1 | Option 2 | note
Priority | 3 | 3 | 
Frequency resource assignment | 4 | 2 | 4 is based on 10 PRB subchannel size 2 is based on 20 PRB subchannel size
Time resource assignment | 5 | 5 | 
Resource reservation period | 0 | 0 | 
DMRS pattern | 1 | 1 | 
2nd-stage SCI format | 2 | 2 | 
Beta_offset indicator | 2 | 2 | 
Number of DMRS port | 1 | 1 | 
Modulation and coding scheme | 5 | 5 | 
Additional MCS table indicator | 0 | 0 | 
PSFCH overhead indication | 1 | 1 | 
Reserved | 2 | 2 | 
Total | 26 | 24 | 

## Slide 9: PSBCH demodulation
The number of S-SSB per one period
  1 S-SSB
Relative velocity
  30km/h (TDLA30-180)

## Slide 10: PSFCH demodulation
Feedback mode
  NACK only
Test metric
  Pr(NACK miss)<1% and Pr(DTX to NACK)<1%
PSFCH periodicity
  1 periodicity
Number of cyclic shift pair
  1 cyclic shift pair
Relative velocity
  30km/h (TDLA30-180)

## Slide 11: Draft CR
Companies volunteering for draft CR are encouraged to provide draft CR for single link tests by referring to the following table in RAN4#98e.
Test case | Volunteer company | Note
General part | Intel | 
PSSCH demodulation test | LG Electronics | 
PSCCH demodulation test | Intel | 
PSBCH demodulation test | CATT | 
PSFCH demodulation test | MediaTek |