## Slide 1: WF on MPR&AMPR simulation assumption for PC2 intra-band contiguous UL
Skyworks Solutions Inc., Qualcomm
R4-2016910
3GPP TSG-RAN WG4 Meeting #97-e
Electronic meeting, 2 – 13 November 2020

## Slide 2: Background on architecture
Current implementations discussed in “WF on RF requirements for PC2 intra-band contiguous UL CA”:
Option 1: PC2 (26dBm) supported with one 26dBm PA supporting 200MHz BW
  baseline for PC3 and could be the baseline for PC2 (measurement input were provided at this meeting)
  UL MIMO can be supported on top of UL CA with an additional path
Option 2: PC2 (26dBm) supported with two 26dBm PA supporting 100MHz BW each
  can be accommodated by the MPR of Option 1 as we did for PC3
  UL MIMO is not supported on top of UL CA
Option 3: PC2 (26dBm) supported with two 23dBm PA supporting 200MHz BW each:
  RIMD issue is more severe as it is in band and since single CC MPR for TxDiv is not yet agreed we don’t really have a baseline for this. I think we could still accommodate based on the 1 PA case with an additional MPR.
  UL MIMO could be supported on top of UL CA but may require additional MPR vs UL CA case.

## Slide 3: WF on Scope
Current version assumes all three options in “WF on RF requirements for PC2 intra-band contiguous UL CA” need to be supported, but in case of down selection the WF will be revised
Whether same MPR table can be used for more than one option, or delta MPR is enough compared to baseline 1PA MPR is FFS
In order to finalize option 3, single CC MPR based on Tx Diversity needs to be available and additional MPR may be required for UL MIMO.
Whether different MPR values are defined for class B and class C UL CA is FSS
Whether option 2 is allowed for class B UL CA is FSS

## Slide 4: WF on allocations and waveforms
Inner/outer contiguous allocations definition for PC3 is used to evaluate MPR and AMPR
Inner/outer1/outer2 non-contiguous allocations definition for PC3 is used to evaluate MPR and AMPR
Both CP-OFDM and DFT-s-OFDM waveforms are used.
Channel BW configurations valid for class B and C should be evaluated
  Class B: at least 20MHz+20MHz 15kHz SCS and 50MHz+50MHz 15kHz SCS
  Class C: at least 60MHz+100MHz 30kHz SCS and 100MHz+100MHz 30kHz SCS
MPR based on ACLR and SEM agreements in “WF on RF requirements for PC2 intra-band contiguous UL CA” are evaluated based on a number of inner/outer contiguous and inner/outer1/2 non-contiguous allocation cases
NS-04 A-MPR for -13dBm/MHz IM3 and -25dBm/MHz IM3 are evaluated especially for 1RB+1RB non-contiguous and Full+Full allocation cases

## Slide 5: WF on assumptions for MPR A-MPR evaluation
4dB post PA losses
Equal PSD and Equal back-off power split
For 2 PA cases antenna isolation assumption is 10dB
Option 1 and 2 based on 26dBm PAs: each PA is calibrated for 31dBc ACLR at 25dBm with 20MHz 100RB0 DFT-s-OFDM QPSK waveform
Option 3 based on 23dBm PAs: each PA is calibrated for 30dBc ACLR at 22dBm with 20MHz 100RB0 DFT-s-OFDM QPSK waveform