## Slide 1: WF on testability enhancements to support the verification of RF requirements for inter-band (FR2+FR2) CA
Anritsu
R4-2017595
3GPP TSG-RAN WG4 Meeting #97-e
Online, 3rd – 13th Nov 2020
Agenda: 13.1.3
E-mail title: [97e][331] FR2_enhTestMethods
Topic: 3
WI: FR2_enhTestMethods

## Slide 2: Background: Use of offset antenna test method
The way forward [2] was approved at RAN4 #96-e to conduct a further study to determine whether non co-located test antennas for FR2 DL inter-band CA verification is feasible from the perspective of ∆PSD at the UE after spatial filtering.
 |  | Antenna offset in distance / angle | 
 |  | 50 mm | 100 mm
Range length | 1200 mm | 2.4 deg | 4.8 deg
 | 1000 mm | 2.9 deg | 5.7 deg
 | 800 mm | 3.6 deg | 7.1 deg
Expected angular offset between 2 antennae
Radiation pattern of 2x8 antenna.

## Slide 3: Contributions to sub-topic 3
T-doc number | Company | Title
R4-2014265 | Qualcomm Incorporated | On impact of non-co-located test antennae for FR2 inter-band testing
R4-2014492 | Fraunhofer HHI, Fraunhofer IIS | Beam correspondence performance measurement improvements of FR2 UEs using carrier aggregation and shared antenna arrays
R4-2014687 | Anritsu Corporation | Testability of FR2 inter-band DL 2CA EIS by non co-located antenna
R4-2014921 | Apple Inc. | Impact of AoA offset on inter-band CA PSD difference

## Slide 4: Status summary of the 1st round
Issue 3-1-1: Feasibility of offset test antennae for FR2 inter-band testing | It appears that views have converged that the offset test antenna method is feasible for IBM, at least for the configurations for which UE RF core requirements are currently defined. It is recommended to capture this outcome in the WF; all open issues are part of Issue 3-1-2.
Issue 3-1-2: Remaining open issues with offest test antennae for FR2 inter-band testing | It is recommended to capture a list of remaining open issues with offset test antenna method, such as QoQZ, calibration, CBM, handling additional IBM configurations
Issue 3-2-1: Beam correspondence for FR2 inter-band CA and shared antenna arrays | Further discussion to clarify the problem statement and potential questions/open issues is needed in the 2nd round. This topic can be part of the WF and, if consensus can be achieved during the 2nd round discussion, an LS to RAN1 could be one possible outcome.
Status of the discussions as of end of the 1st round are extracted below from the summary [1].

## Slide 5: Outcome on issue 3-1-1
Outcome on the feasibility of offset test antennae for FR2 inter-band testing
RAN4 is converging to a view that the offset test antenna method is feasible for IBM at least for the configurations for which UE RF core requirements are currently defined. (i.e. Refsens and DL spherical coverage) Remaining open issues on the next slide shall be studied further.
Conditions on which the offset test antenna method has been studied:
Band combination CA_n260-n261
Range length of the test system 800 mm to 1200 mm
Antenna offset distance 50 mm to 100 mm
UE power class PC3
UE beam management Independent BM
The feasibility for other conditions (e.g. band combination, power class, range length…) is FFS.

## Slide 6: Way forward on issue 3-1-2
Companies are encouraged to study the feasibility of the offset test antenna method
especially with the following open issues which were identified during RAN4#97-e.
1) Impact on QZ size and quality
2) Potential to trigger different choice of optimum UE beam facing each source and impact on beam management performance
3) Applicability of potential power class specific manufacturer declarations (e.g. PC1 and PC5 may have a different optimum than PC3)
4) Feasibility of the solution for inter-band CA with CBM
5) Feasibility of the solution for inter-band CA with band n262

## Slide 7: Reference
[1] R4-2017429, “Email discussion summary for [97e][331] FR2_enhTestMethods”, Moderator (Apple Inc.), RAN4 #97-e, Online
[2] R4-2012715, “WF on the inter-band CA within FR2 objective”, Anritsu, RAN4 #96-e, Online
[3] R4-2014492, “Beam correspondence performance measurement improvements of FR2 UEs using carrier aggregation and shared antenna arrays”, Fraunhofer HHI, RAN4 #97-e, Online

## Slide 8: Appendix A:
Applicability of offset antenna method to inter-band CA test (DL test for now)
UE beam management | Band combination |  | 
 | 28 + 28 GHz (L+L) | 39 + 39 GHz (H+H) | 28 + 39 GHz (L+H)
CBM | FFS2 | FFS2 | N/A
IBM | FFS2 | FFS2 | Feasible 1
Note 1: Under limited conditions listed on slide 5. FFS with open issues on slide 6. Note 2: Described as FFS due to the lack of band combination definitions in Rel-16. Note 3: 28 GHz denotes band n257/n258/n261. 39GHz denotes band n259/n260. CBM: Common Beam Management IBM: Independent Beam Management |  |  |