## Slide 1: 3GPP TSG-RAN WG4 Meeting #97-e R4-2017675 Electronic Meeting, 2nd Nov - 13th Nov, 2020
Huawei, HiSilicon
Way forward on NR URLLC BS performance requirements

## Slide 2: Background
The following WFs were approved:
  R4-1915913: Way forward on NR URLLC demodulation and CSI requirements, RAN4 #93
  R4-2002429: Way forward for NR BS URLLC performance requirements, RAN4 #94-e
  R4-2005528: Way forward for NR BS URLLC performance requirements, RAN4 #94bis-e
  R4-2008810: Way forward for NR BS URLLC performance requirements, RAN4 #95-e
  R4-2012649: Way forward for NR BS URLLC performance requirements, RAN4 #96-e

## Slide 3
Agreements:
Whether to clarify the safety statement in specification
  Agreement: capture following note in WF, not include into specification. ( no other companies show views on this topic till now except Huawei, Samsung, Nokia and E///).
    If the URLLC features of 5G NR would be used in safety or mission critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians. It is also important to bear in mind that the demodulation requirements do not take account of all aspects of system operation (for example RF, transmitter, internal interfaces, higher layer protocol software etc.).
BS demodulation requirements of high reliability for FR1
SNR values (dB) in specs (based on simulation results in R4-2015629):
  Applicability rule for FDD and TDD
    PUSCH aggregation factor for 15 kHz SCS: The requirements for PUSCH with aggregation for 15kHz can be tested either by configuring n8 and the DDDSU TDD pattern or by configuring FDD with aggregation level n2.
PUSCH BS demodulation requirements of high reliability:
 |  | 15 kHz/5 MHz | 15 kHz/10 MHz | 30 kHz/10 MHz | 30 kHz/40 MHz
TS 38.104 | Type A | [-8.5] | [-9.3] | [-8.2] | [-10.3]
 | Type B | [-8.2] | [-9.8] | [-8.2] | [-10.2]
TS 38.141 | Type A | [-7.9] | [-8.7] | [-7.6] | [-9.7]
 | Type B | [-7.6] | [-9.2] | [-7.6] | [-9.6]

## Slide 4
Agreements:
BS demodulation requirements of high reliability for FR2
  Waveform: CP-OFDM
  TDD pattern: DDDSU, S=10:2:2
  Aggregation factor for TDD: n8 for DDDSU with note
    Note: The intention of this configuration is to have two effective transmissions of the transport block. To achieve this for the standard TDD pattern captured in this table, a value of n8 is necessary.
  Applicability rule for TDD with different UL-DL patterns: The same requirements are applicable to TDD with different UL-DL patterns and different aggregation factor configurations under assumption that two effective transmissions of the transport block are generated.
  Channel model: TDLA30-300 Low
  DM-RS: 1+1
  HARQ process number: 4
  RV sequence for 4 HARQ re-transmission: {0,3,0,3} with note
    Note: The effective RV sequence is {0,2,3,1} with slot aggregation
  SCS/BW: Both of 60 kHz and 120 kHz for both of 50 MHz and 100 MHz with applicability rule.
    Applicability rule: Only 1 SCS and 1 BW need to be tested based on the base station declaration and if there is no requirement for the declared BS bandwidth then the next lower requirement bandwidth is used.
  No PTRS
PUSCH BS demodulation requirements of high reliability:

## Slide 5
Simulation assumption for BS FR2 demodulation requirements of high reliability
PUSCH BS demodulation requirements of high reliability:
Parameter |  | Value
Transform precoding |  | Disabled
SCS/BW |  | Both of 60 kHz and 120 KHz for both of 50 MHz and 100 MHz
Uplink-downlink allocation for TDD (Note 1) |  | 60 kHz and 120kHz SCS: 3D1S1U, S=10D:2G:2U
Antenna configuration |  | 1x2, Low
Number of layers |  | 1
HARQ | Maximum number of HARQ transmissions | 4
 | RV sequence | 0,3,0,3 (Note 2)
DM-RS | DM-RS configuration type | 1
 | DM-RS duration | Single-symbol DM-RS
 | Additional DM-RS position | Pos1
 | Number of DM-RS CDM group(s) without data | 2
 | Ratio of PUSCH EPRE to DM-RS EPRE | -3 dB
 | DM-RS port(s) | {0}, {0, 1}
 | DM-RS sequence generation | NID0=0, nSCID =0
Time domain resource assignment | PUSCH mapping type | B
 | Starting symbol | 0
 | Allocation length | 10
 | PUSCH aggregation factor | n8 (Note 3)
Frequency domain resource assignment | RB assignment | Full applicable test bandwidth
 | Frequency hoping | Disabled
Code block group based PUSCH transmission |  | Disabled
Propagation condition and correlation matrix |  | TDLA30-300 Low
PT-RS configuration | Frequency density (KPT-RS) | Disabled
 | Time density (LPT-RS) | Disabled
Testing metric |  | Target BLER: 10-2 (Calculate the target BLER after all transmission)
Note 1: The same requirements are applicable to TDD with different UL-DL patterns and different aggregation factor configurations under assumption that two effective transmissions of the transport block are generated. Note 2: The effective RV sequence is {0,2,3,1} with slot aggregation Note 3: The intention of this configuration is to have two effective transmissions of the transport block. To achieve this for the standard TDD pattern captured in this table, a value of n8 is necessary. |  | 

## Slide 6: PUSCH demodulation requirements for low latency
Agreements:
FR1 URLLC demodulation requirements for PUSCH mapping Type B
    SNR values in specs (based on simulation results in R4-2015629)
FR2 URLLC demodulation requirements for PUSCH mapping Type B
  Waveform: CP-OFDM only
  Maximum HARQ re-transmission: 1
  No PTRS
  SCS/BW: Both of 60 kHz and 120 kHz for both of 50 MHz and 100 MHz with applicability rule.
    Applicability rule: Only 1 SCS and 1 BW need to be tested based on the base station declaration and if there is no requirement for the declared BS bandwidth then the next lower requirement bandwidth is used.
  Symbol length: 4
  DM-RS: 1+0 for symbol length of 4
  MCS: MCS5 from Table 3
 | 15 kHz/5 MHz | 15 kHz/10 MHz | 30 kHz/10 MHz | 30 kHz/40 MHz
TS 38.104 | [0.6] | [0.2] | [0.4] | [-0.1]
TS 38.141 | [1.2] | [0.8] | [1.0] | [0.5]

## Slide 7: Simulation assumption for FR2 URLLC demodulation requirements for PUSCH mapping Type B
Parameter |  |  | Value
Transform precoding |  |  | Disabled
SCS/BW |  |  | Both of 60 kHz and 120 KHz for both of 50 MHz and 100 MHz
Uplink-downlink allocation for TDD |  |  | 60 kHz and 120kHz SCS: 3D1S1U, S=10D:2G:2U
Antenna configuration |  |  | 1x2, Low
Number of layers |  |  | 1
MCS |  |  | MCS5 (Table 3)
HARQ | Maximum number of HARQ transmissions |  | 1
 | RV sequence |  | 0
DM-RS | DM-RS configuration type |  | 1
 | DM-RS duration |  | Single-symbol DM-RS
 | Additional DM-RS position |  | 0
 | Number of DM-RS CDM group(s) without data |  | 2
 | Ratio of PUSCH EPRE to DM-RS EPRE |  | -3 dB
 | DM-RS port(s) |  | {0}, {0, 1}
 | DM-RS sequence generation |  | NID0=0, nSCID =0
Time domain resource assignment | PUSCH mapping type |  | B
 | Starting symbol |  | 0
 | Allocation length |  | 4
 | PUSCH aggregation factor |  | 1
Frequency domain resource assignment | RB assignment |  | Full applicable test bandwidth
 | Frequency hoping |  | Disabled
Code block group based PUSCH transmission |  |  | Disabled
Propagation condition and correlation matrix |  |  | TDLC300-100 Low
PT-RS configuration |  | Frequency density (KPT-RS) | Disabled
 |  | Time density (LPT-RS) | Disabled
Testing metric |  |  | 70% maximum throughput
Note 1: The same requirements are applicable to TDD with different UL-DL patterns and different aggregation factor configurations under assumption that two effective transmissions of the transport block are generated. Note 2: The effective RV sequence is {0,2,3,1} with slot aggregation Note 3: The intention of this configuration is to have two effective transmissions of the transport block. To achieve this for the standard TDD pattern captured in this table, a value of n8 is necessary. |  |  | 

## Slide 8: Rel-16 URLLC BS features
Agreements:
Whether to define performance requirements for PUSCH repetition type B
  Postpone the decision in next RAN4 meeting, and till Dec 2020 focused on Rel-15 test cases open issues.
Whether to define performance requirements for Inter-UE multiplexing
  Agreement: Do not define the performance requirement for inter-UE multiplexing as no demodulation impact is expected.

## Slide 9: PUSCH demodulation requirements CR work split
Specifacation | Requirements title | CR Specifacation | Frequency range | CR work | CR Responsibility
BS demodulation (38.104/38.141-1/38.141-2) | FRC for all test cases | 38.104 | FR1 | FRC | Nokia
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | FRC | Ericsson
 |  | 38.141-2 | FR1 | FRC | Huawei
 |  |  | FR2 | FRC | Samsung
 | Test methodology | 38.104? | N/A | Test methodology | Nokia
 |  | 38.141-1 | N/A | Test methodology | Ericsson
 |  | 38.141-2 | N/A | Test methodology | Nokia/Huawei
 | Test applicability for all test cases | 38.141-1 | FR1 | Test applicability | Huawei
 |  | 38.141-2 | FR1 | Test applicability | Ericsson
 |  |  | FR2 | Test applicability | Ericsson
 | Requirements for PUSCH with ultra-low BLER target (10-5) | 38.104 | FR1 | Requirements | Nokia
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Ericsson
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | Ericsson
 |  |  | FR2 | N/A | N/A
 | Requirements for PUSCH with aggregation factor configured | 38.104 | FR1 | Requirements | Huawei
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Huawei
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | DoCoMo
 |  |  | FR2 | Requirements / Measurement of Performance requirements Annex C.3 | Huawei
 | Requirements for PUSCH for mapping Type B with low number of symbols | 38.104 | FR1 | Requirements | Nokia
 |  |  | FR2 | FFS | Samsung
 |  | 38.141-1 | FR1 | Requirements/Measurement of Performance requirements Annex C.3 / Measurement system set-up Annex D | Huawei
 |  | 38.141-2 | FR1 | Requirements / Measurement of Performance requirements Annex C.3 | DoCoMo
 |  |  | FR2 | Requirements / Measurement of Performance requirements Annex C.3 | Intel