## Slide 1
3GPP TSG-RAN WG4 Meeting # 98-e R4-2100105
Electronic Meeting, 25th January– 5th Febuary, 2021
Motivation for new WI on PC2 for NR band n34

## Slide 2: Justification
There are challenges on the uplink coverage of high frequency, and particularly in the discontinuity of TDD mode. Concerning the imbalance of uplink and downlink budget, we need to increase the uplink coverage. RAN4 has completed PC2 HPUE feature to improve the uplink coverage for 5G SA deployments on NR bands n41, n77, n78 and n79 in Rel-15 NR WI. NR Band n34 with frequency range 2010-2025MHz is an NR TDD band, the limit of 2GHz 5G NR uplink coverage lead to the imbalance coverage of uplink and downlink. In addition, 5G NR UE may use a larger transmission bandwidth, if increase bandwidth but not increase the UE transmission power, power spectral density will reduce, and the uplink coverage will be reduced. It is more urgent need to increase the UE output power for n34 in order to guarantee uplink coverage.
It is proposed to specify Power Class 2 UE for NR band n34 supporting +26 dBm. The PC2 n34 UE maximum output power can be reference PC2 n41, n77,n78,n79 HPUE, defined as +26dBm in this Work Item. This Work Item is to develop a new feature to enable HPUE (power class 2) for NR band n34.

## Slide 3
Objective of Core and performance part WI
The core objectives of the WI are:
Introduction of NR band n34 to support high power UE (Power class 2)
Specify RF characteristics for n34, including UE maximum output power, Tx power tolerance and UL-MIMO for PC2 n34.
Release independent issue is to be considered for PC2 n34
The performance objectives of the WI are:
Release independence requirements if needed (TS 38.307)

## Slide 4
Thanks!