## Slide 1: WF on NR MIMO OTA
vivo, CAICT
3GPP TSG-RAN WG4 Meeting #98-e R4-2103913
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda item: 11.1.1
Document for: Approval

## Slide 2: Test Method
System implementation of FR2 3D-MPAC system
  Keep the probe locations the same among system implementations at this time, but enhanced implementation or solution can be considered by RAN4 in future
  Further study how to address the FR2 blocking issue
Conclude the agreed 36 test points for FR2 MIMO OTA testing
Usage of gNB beams for FR1 MIMO OTA testing :
  Beam1_H, Beam1_v, Beam2_H, Beam2_v are mapped to CE input ports 1, 2, 3 and 4 in 4x4 case and Beam1_H, Beam1_v are mapped to CE input ports 1 and 2 in 2x2 case. 2 strongest beams selected for 4X4 and 1 strongest selected for 2X2.
  The beams are not combined in the actual test. The gNB emulator ports are connected to each CE input port, where each port corresponds a channel model realization with one polarization of one beam.

## Slide 3: System validation
Channel model validation
  For spatial correlation validation, only Vertical validation is required.
  gNB Beams Usage Criteria for FR1 MIMO OTA Channel Model Validation
    Option 1: Beam specific: The two strongest beams are measured separately applied for all channel model validation factors (agreed as baseline, further define validation pass/fail limit based on this approach)
    Option 2: Combined beams: The two strongest beams are combined at the input of the channel emulator for validation of spatial correlation. The PDP validation is done separately for each beam in this case.
  For FR1 and FR2 channel model validation, adopt 40dB threshold for cluster power
    Further study the impact of 40dB threshold on UE throughput performance with CDL-A channel model for FR2
  Conclude the existing PSP validation procedure with 5cm radius as baseline
  Channel model validation limit
    Further discuss and define the reference before RAN4 specify the actual values

## Slide 4: Test Parameters for requirements
Test Parameters for FR1 requirements
  RAN4 confirms that the CDL-C UMa channel model is adopted to define FR1 4x4 MIMO OTA requirements
  For FR1 2x2 MIMO OTA requirements, the channel model is FFS. Candidate options are: CDL-A UMi, CDL-C UMa, CDL-C UMi. Other options are not precluded
  PRS-EPRE-MAX for band frequency <3GHz, 40MHz bandwidth
    [-77dBm/30kHz] (starting point)
    Note: This value is pending on further verification and confirmation from TE vendors/Test labs for the feasibility. Further discuss and revise the value is not excluded
  PRS-EPRE-MAX for band frequency >3GHz, 10MHz and 40MHz bandwidth needs further study
    When define the maximum downlink power, the path loss induced by different channel models need to be considered
  Minimum number of slots for FR1 MIMO OTA testing
    For bands >1GHz: 20k for 30kHz SCS, 10k for 15kHz SCS;
    For bands <1GHz, [20k] for 15kHz SCS;
    Note: The above number of slots are the recommendation value for both FR1 MIMO OTA test lab alignments and FR1 MIMO OTA UE performance requirements introduction
    Test labs are encouraged to bring more analysis/measurement results with different number of slots for comparison purpose

## Slide 5: NR MIMO OTA requirements
Figure of Merit for NR MIMO OTA requirements
  For FR1 MIMO OTA performance requirements:
    Restriction of Pmode at 70%TP for 40MHz CHBW.
      For 40MHz CHBW, the 11 of total 12 PMODE should reach 70%TP as a starting point based on the current assumption of PRS-EPRE-MAX value
    Additional restriction of Pmode for 10MHz and 40MHz CHBW.
      Adopt Pmode at 90%TP as an additional restriction
        90% TP, [TBD] of total 12 as starting point
        Companies are encourage to bring more analysis and measurement data.
  For FR2 MIMO OTA performance requirements:
    How to treat the orientations that cannot reach 70% TP
      how to treat the missing points can not reach 70%TP for MASC calculation is FFS
      additional criterion on how to treat the number of missing points should be further studied

## Slide 6: Next steps
  Further study the proper Channel model for FR1 2x2 MIMO OTA requirements
  Discuss the pass/fail limit and reference figure of channel model validation
  Further discuss testing parameters for requirements (e.g. Maximum downlink power for bands>3GHz)
  Further discuss the Figure of Merit for FR1 and FR2
  Measurement results of FR1 or FR2 UEs are encouraged for discussion
  Channel model validation results for FR2 channel models are encourages
  Analysis on MU evaluation of FR2 blocking issue
  FR2 simulation results of UE performance are encouraged