## Slide 1: Requirement framework for Inter-band CA with CBM
RAN4#98-Bis-e R4-2104491
e-Meeting, Apr. 2021
Agenda Item: 8.3.2.1.1
Qualcomm Incorporated

## Slide 2: Topology study seems necessary for progress
Generalized definition of CBM [2]:
  Single beam management reference signal (BMRS), common to both bands
  Both bands are not restricted to using a common ‘beam’
CBM not restricted to certain types of band pairs [1]
  Early assumption was to ‘extend’ intra-band operation for overlapping or adjacent bands
  Topologies other than extended intra-band operation are better suited to L+M or L+H
    Performance of ext. intra-band deteriorates significantly when fractional BW of combined coverage > 20%
There is no convergence on requirement framework for CBM CA UEs
  Different architectures need different performance aspects to be verified
  Examples of problems:
    Can skip EIS spherical coverage requirement for all topologies of CBM UEs?
    Specifying PSD difference in test condition for EIS
    Identifying ACS/IBB requirement applicability (contiguous? NC?)
Reference architecture assumptions needed to complete requirement framework
  Requirement framework should accommodate all identified implementations

## Slide 3: CBM UE topologies
Two broad categories for band pairs sharing a single beam management reference signal
  Most practical topologies will lie somewhere between extreme examples described in figures
‘Single-beam’: single beam forming network shared by both bands (‘SB CBM’) top figure
  This category favors simplicity, and the simplest variant is considered here:
    Antenna-to-ADC resources shared across bands (same antenna, LNA, AGC, etc.)
‘Multi-beam’: multiple beam forming networks, each dedicated to one band (‘MB CBM’) bottom figure
  One of the RF chains would have to be aimed ‘blind’ based on beam choice in band with reference signal
  This category favors performance, and the best performing variant is considered here:
    Dedicated RF chain with independent AGC, independent timeline. This variant of MB CBM UE has similar RF hardware complexity as IBM UEs, but has simpler beam management

## Slide 4: Design considerations with challenges
 | Single-beam CBM | Multi-beam CBM
Beam management | Essentially single CC treatment, much simpler than IBM. | Still single CC treatment. UE must additionally set up 1:1 spatial association between beams in one band to beams in second band (‘Inter-band beam mapping’) (One of the RF chains would have to be aimed ‘blind’ based on beam choice in band with reference signal)
RF | NF, Gain must be optimized over both bands AGC state, beam switching common to both bands | Optimized RF performance for each band Independent AGC and beam switching timelines can be maintained for each band
Motivation | Optimized for simplicity | Optimized for MRTD > CP and RF performance (equivalent to IBM UE under single AoA conditions)
Left for UE vendor to decide on feasibility of each option and implementation details associated with it (split array [3], shared vs unique resources, etc)

## Slide 5: Performance expectations by topology choice
(assume 1CC+1CC test condition) | Single-beam CBM | Multi-beam CBM
De-mod Performance | Impacted by : shared gain state for both bands SNR cannot always be optimized for both bands common time-line MRTD of O(ms) will degrade throughput in dynamic scenarios | As good as IBM UE for single AoA condition SNR can be optimized for both bands MRTD of O(ms) can be absorbed without throughput degradation compared to single CC DL performance.
EIS, including REFSENS and spherical coverage, relative to single CC DL performance | Impacted by : shared gain state for both bands SNR cannot always be optimized for both bands beam squint SNR further compromised due to antenna gain reduction wide band operation NF degradation as well as gain droop can be significant | Impacted by: UE’s inter-band beam mapping Beam squint, RF gain droop and NF degradation no worse than single band Same degradation mechanisms considered in DRIB for IBM UEs
Robustness to ACS/IBB | Same as intra-band non-contiguous CA | As good as IBM UE for single AoA condition

## Slide 6: Considerations for CBM UE RF requirements
Requirements must be:
  Implementation-agnostic
  Inclusive of all reasonable implementations
The identified implementation possibilities have different mechanisms that limit performance
  Requirements must check for superset of degradation mechanisms
Deployment link budgets should be aligned between CBM and IBM UEs
  Requirements for existing IBM inter-CA have already shaped network planning and deployment
  Link budgets will be compromised if CBM UEs have significantly different RF performance compared to IBM UEs

## Slide 7: Requirement framework (what to check for?)
Requirement (below): | Single-beam CBM | Multi-beam CBM | Proposed unified requirements for CBM UEs | Justification
MRTD | ( for reference only: to be discussed in RRM session) |  |  | 
REFSENS | UE degradation mechanisms Beam squint wideband gain and NF variation | UE degradation mechanisms Inter-band beam mapping mechanisms considered in DRIB,x | Based on IBM inter-band CA | Intra-band type requirement for REFSENS cannot be used, it would force both bands to share direction for REFSENS testing, which is too restrictive for MB CBM UEs DRIB,p from IBM is reasonable upper bound for all CBM due to link budget reasons
EIS Spherical Coverage |  |  | Based on IBM inter-band CA | Intra-band CA argument to skip common spherical coverage check cannot be used due to MB CBM UEs’ dependence on inter-band beam mapping DRIB,s from IBM is reasonable upper bound for all CBM due to link budget reasons
ACS/IBB | Effect of receiver filtering choices |  | Based on IBM inter-band CA | IBM CA wording suitable for both SB and MB CBM. In case of overlapping bands, interferer of tested band avoids DL of the other band
PSD condition for EIS test | Equal PSD adjustment required for band-to-band differences | PSD mismatch ok like in IBM requirements | (limit to) nominally equal PSD | SB CBM UEs are more restrictive. Like intra-band CA case, these UEs cannot accommodate large PSD difference

## Slide 8: Proposals
Adopt ‘unified requirement framework’ →
Requirements apply in both conditions to verify that beam squint related degradation is not excessive:
  Beam management reference signal in tested band
  Beam management reference signal in non-tested ‘other’ band
See draft CR [4] for spec. language proposal
Requirement: | Proposed unified requirement framework for CBM UEs
REFSENS | Based on IBM inter-band CA
EIS Spherical Coverage | Based on IBM inter-band CA
ACS/IBB | Based on IBM inter-band CA
PSD condition for all EIS test | (limit to) nominally equal PSD

## Slide 9: References
R4-2103326 Email discussion summary for [98e][139] NR_RF_FR2_req_enh2_Part_2, Moderator (Qualcomm)
R4-2103399, ‘WF on FR2 UEs that support inter-band DL CA with CBM’, Samsung, RAN4#98-e
R4-2100893, ‘Discussion on IBM inter-band CA within same frequency group’, Samsung, RAN4#98-e
R4-2104990, ‘Draft CR to 38.101-2 on requirements for UEs that support inter-band CA with CBM’, Qualcomm, RAN4#98-Bis-e