## Slide 1: WF on combinations not for block approval and their handling
Apple
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic Meeting, April 12th – 20th, 2021
R4-2105334

## Slide 2: Background
UE band combination basket work items block approval process has been implemented since LTE and continued in NR.
The framework has successfully facilitated the TR TP review process and improved RAN4 work efficiency on developing the UE RF requirements for majority of band combinations.
Nonetheless, there are certain band combinations which may require additional technical justifications or requirements not covered by the standard basket TR TP format and may not be suitable for block approval process.
This WF is intended to provide guidelines for FR1 band combinations not for block approval and their handling.

## Slide 3: FR1 Band Combinations Not for Block Approval
Inter-band DL CA with intra-band contiguous or non-contiguous UL CA which has potential IMD impact to the simultaneous Tx/Rx cross-band DL. No simultaneous Tx/Rx to victim DL band is still applicable to block approval with a clarification note in the TP.
  Develop IMD analysis framework and related MSD specification tables.
  Example: CA_nX-nY(2A) or CA_nX-nY(2A)-nZ with UL CA_nY(2A)
Inter-band combinations with three UL CCs in two bands. If more than one CC in one band, the CC should be contiguous. No simultaneous Tx/Rx to victim DL band is still applicable to block approval with a clarification note in the TP.
  Triple-beat analysis should be provided for two and three DL band cases for cross-band MSD in simultaneous TX/RX DL bands.
  Develop IMD and triple-beat analysis framework and related MSD specification tables with three UL CC cases as a priority.
  Example: CA_nX-nYB/C or CA_nX-nYB/C-nZ with UL CA_nX-nYB/C
Intra-band UL CA with two CCs where A-MPR requirements have not been specified.

## Slide 4: FR1 Band Combinations Not for Block Approval
Inter-band combinations with three or more bands below 1 GHz with UL in one or two bands
  Example: DC_8-20_n28
Inter-band combinations with two bands below 1 GHz and UL in two bands not yet specified in E-UTRA
  Example: DC_20_n28
Inter-band combinations with three or more bands within 1 – 2.2 GHz with UL in one or two bands not yet specified in E-UTRA.
  Example: CA_1A-3A-11A (already specified in E-UTRA, for illustration only)

## Slide 5: FR1 Band Combinations Not Allowed in R17
Intra-band contiguous EN-DC with new bandwidth class, such as classes AC and CB: Need a new feature defined.
Intra-band contiguous UL CA with three CCs (feature not yet defined)
UL CA with three or more non-contiguous CCs (feature not yet defined) including
  Inter-band UL CA with UL in three or more bands
  Intra-band non-contiguous UL CA with three or more discrete UL CCs
  Inter-band UL CA consisting of intra-band non-contiguous UL CA
Whether inter-band combinations with two contiguous UL CCs in each of the two UL bands which has potential IMD impact to the simultaneous Tx/Rx victim DL band is allowed or not will be further discussed.

## Slide 6: Way Forward
A specific agenda item is created for band combinations not for block approval for the entire length of the meeting. Band combinations with discussion papers or more discussions needed after flagging can be treated in this agenda.
Discussion paper can be associated with a corresponding TP for TR for approval.
If new requirements not currently captured in basket WI TRs are needed (such as MSD caused by triple-beat IMD), adding new clauses in the existing basket WI TRs to capture these requirements.
Already proposed band combinations which are not allowed in R17 should be removed from the R17 band combination request list.