## Slide 1: Way forward on MPR and AMPR PC2 for intra-band UL contiguous CA
Skyworks Solutions Inc., …
R4-2105336
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic meeting, 12 – 20 Apr. 2021

## Slide 2: Background: RAN and RAN4 agreements
RAN agreements in [6] Guidelines for Combinations Not for Block Approval and relevant to this WF:
Intra-band contiguous EN-DC with new bandwidth class, such as classes AC and CB: Need a new feature defined)
Intra-band UL CA with 2 CCs where A-MPR requirements have not been specified (in basket WID not for block approval)
Intra-band contiguous UL CA with 3 CCs (feature not yet defined)
UL CA with three or more non-contiguous CCs (feature not yet defined) including
  Inter-band UL CA with UL in three or more bands
  Intra-band non-contiguous UL CA with three or more discrete UL CCs
  Inter-band UL CA consisting of intra-band non-contiguous UL CA
RAN4 agreements this meeting and relevant to this WF:
MSD related to IMDs of intra-band UL CA part (contiguous or non-contiguous) needs to be analyzed, Develop a framework for such analysis, this is also pending agreement that such cases are not for block approval
NR contiguous and non-contiguous UL CA IMDs should be analyzed for band protection based on filter and IMD order. A framework should be created, this is also pending agreement Whether such cases should be treated within the intra-band NR CA basket or in combinations not for block approval

## Slide 3: WF: Detailed handling of cases with intra-band UL CA part
Combinations types with intra-band ULCA part not allowed that should be removed from 38.101-1 or 38.101-3 and from basket and cannot be requested for R17:
CA or DC with 3 non-contiguous UL CCs: UL configuration A/B/C in one band with NR (2A) in a second band
NRCA or DC with contiguous UL CA in two bands: UL configuration NR B/C in one band with NR B/C in a second band
  FFS if some cases can be proposed in the not for approval AI: For example if non simultaneous Tx/Rx TDD-TDD
Combinations types with intra-band ULCA part not for block approval:
CA or DC with 2 UL CCs in one band: NR UL configuration B/C/2A in a single band
CA or DC with 3 UL CCs : UL configuration A in one band with B/C in a second band
CA or DC with 4 UL CCs: UL configuration LTE B/C in one band with NR B/C in a second band
Applies to intra-band, 2 band and 3 band combination containing at NR UL CA in one band
Once 1/2/3 band combinations are completed, higher combinations can be submitted to block approval with draft CRs
Combinations types with intra-band UL CA that can still be for block approval:
Any of the above case where the DL in the same band, second band or third band does not support simultaneous Tx/Rx with the UL CA band since the corresponding DL band cannot be subject to MSD
  For example TDD intra-band UL CA, TDD-TDD two bands with non support for simultaneous TX/RX (be careful the issue may still exist in the third DL band case if it is FDD or if simultaneous Tx/Rx)
  A TP for block approval can be used with a text justifying why the MSD is not possible (i.e related to simultaneous Tx/Rx)

## Slide 4: WF: handling of band protection issues with intra-band UL CA part
When NR UL CA B/C or 2A in introduced for intra-band UL, there may be issues with band protection that this band has to fulfil if simultaneous TX/Rx is possible
Some criteria is provided later in this WF to determine which bands may be an issue
Given this is relatively straight forward it should be feasible to handle this directly in the NR intra-band basket with a TP.
If needed proponent can always submit a discussion paper to the agenda item not for block approval to get experts guidance
WF: For the cases where -50dBm/MHz band protection cannot be fulfilled, the proponent must provide a resolution with UL restriction, relaxed protection level and seek approval from the owners of this band
WF: A separate input to CA coexistence Table 6.5A.3.2.1-1 should be specified in 38.101-1 with the agreed exception

## Slide 5: Background: UL CA IMDs interfering with other bands and creating band protection or MSD issues
For NR contiguous UL CA with MPR applied:
  IMD3 can reach up to 200MHz OOB with -13dBm/MHz
  IMD5 can reach up to 400MHz OOB with -30dBm/MHz for NS01 and -25dBm/MHz for NS04
  IMD7 can reach up to 600MHz OOB with -45dBm/MHz for NS01 and -35dBm/MHz for NS04
For NR non-contiguous UL CA with MPR applied:
  IMD 3 can reach up to 600MHz OOB with -30dBm/MHz
  IMD 5 can reach up to 1200MHz OOB with -45dBm/MHz for NS01 and -25dBm/MHz for NS04
The above levels are further attenuated by the UL band filter and any diplexer
There is only an issue with band that have simultaneous Tx/Rx with the UL band

## Slide 6: WF: band protection analysis for IMDs of UL CA part
To be able to meet -50dBm/MHz band protection level
For intra-band contiguous UL CA
  if any band is subject to UL CA IMD3, at least 37dB rejection is needed from the band filter (DC_40A_n41C and CA_n40A-n41C fall in this case).
  if any band is subject to UL CA IMD5, at least 20/25dB rejection is needed from the band filter for NS01/NS04
  IMDs above IMD7 are not an issue
For intra-band non-contiguous UL CA
  if any band is subject to UL CA IMD3, at least 20/25dB rejection is needed from the band filter for NS01/NS04
  if any band is subject to UL CA IMD5, at least 15dB rejection is needed from the band filter for NS04
  IMDs above IMD5 are not an issue
WF: when NR UL contiguous or non-contiguous CA is introduced in a band the above analysis is conducted, conclusion are provided in a discussion paper and resolution provided if -50dBm/MHz cannot be supported
WF: band 40 protection should be analysed for DC_40A_n41C and CA_n40A-n41C

## Slide 7: WF: MSD analysis for IMDs of UL CA part
To be able to meet -110dBm/MHz interference level in a second band or third band DL:
  For intra-band contiguous UL CA, even with 50/60dB rejection from the filter for NS01/NS04 MSD can occur for a 5MHz channel up to IMD9
  For intra-band non-contiguous UL CA, even with 50/60dB rejection from the filter for NS01/NS04 MSD can occur for a 5MHz channel up to IMD7
  To derive which IMD order may fall in a given victim band the IMD BW must be determined:
    IMD BW is aggregated BW for contiguous UL CA and CC1 BW+ gap BW + CC2 BW for non-contiguous UL CA
    Lowest IMD order falling in victim is 2*( (Aggressor-Victim distance)/(IMD BW) rounded up to the next integer)+1
  Approximate lower order IMD levels before filtering are provided in slide 5 and analysis should be performed at least up to IMD13 for contiguous UL CA and IMD11 for non-contiguous UL CA if filter rejection is less than 20dB.
  Analysis or verification of higher IMD order is not precluded
WF: When introducing an intra-band contiguous or non-contiguous UL CA configuration in a 2band or 3 band inter-band combination, cross-band MSD study should be performed based on IMD order falling in the victim band, the victim band distance and UL band filter attenuation.

## Slide 8: WF: Specification IMDs of UL CA part
To simplify the number of MSDs to be specified it is proposed to specify such cases in 38.101-1 section 7.3A.5Reference sensitivity exceptions due to intermodulation interference due to 2UL CA in tables 7.3A.5-1 and Table 7.3A.5-2 with a separate entry for UL CA case
Similar tables are used for the corresponding section in 38.101-3.
  Example with CA_n1(2A)-n3 and CA_n1(2A)-n3-n34 with CA_n1(2A) as UL configuration
WF: the above table format is used to cature MSDs related to IMDs of UL CA part
  The test point should be chosen for: lowest IMD order of 1RB0 + 1RBmax falling in the smallest victim BW
  Other test points are not precluded but must be justified by regional spectrum restrictions
Band / Channel bandwidth / NRB / Duplex mode |  |  |  |  |  |  |  | Source of IMD
NR CA band combination | NR band | UL Fc (MHz) | UL/DL BW (MHz) | UL CLRB | DL Fc (MHz) | MSD (dB) | Duplex mode | 
CA_n1(2A)-n3 | n1(2A) | 1922.5+1977.5 | 5+5 | 1RB0+1RB25 | 2112.5+2167.5 | N/A | FDD | N/A
 | n3 | N/A | 5 | N/A | 1862.5 | 20 | FDD | IMD3
CA_n1(2A)-n3-n34 | n1(2A) | 1942.5+1977.5 | 5+5 | 1RB0+1RB25 | 2132.5+2167.5 | N/A | FDD | N/A
 | n3 | N/A | 5 | N/A | 1862.5 | N/A | FDD | N/A
 | n34 | N/A | 5 | N/A | 2017.5 | 25 | TDD | IMD3

## Slide 9: WF: Handling of existing and flagged combinations before the meeting
Analysis have been provided in [3]:
The cases in green can stay in spec or introduced in next meeting with TP in AI not for block approval with a simple text justifying that no MSD is needed
The cases in yellow need to provide MSD proposals or technical justification for no MSD
DL | UL | status | IMD BW | IMD order | comment
DC_1A_n7B | DC_1A_n7B | in spec | 50 | 15 | high IMD order => OK
CA_n2A-n48C | CA_n48C | in spec | 50 | 65 | high IMD order => OK
DC_3A/C_n7B | DC_3A_n7B | in spec | 50 | 27 | high IMD order => OK
CA_n3A-n77(2A) | CA_n77(2A) | in spec | 600 | 7 | IMD7 MSD to be analyzed
CA_n3A-n78(2A) | CA_n78(2A) | in spec | 400 | 9 | IMD9 MSD to be analyzed
DC_8A_n79C | DC_8A_n79C | in spec | 200 | 37 | high IMD order => OK
CA_n25A-n41C | CA_n41C | in spec | 190 | 7 | IMD7 MSD to be analyzed
DC_28A_n7B | DC_28A_n7B | in spec | 50 | 69 | high IMD order => OK
CA_n28A-n77(2A) | CA_n77(2A) | in spec | 600 | 11 | high IMD order => OK
CA_n28A-n78(2A) | CA_n78(2A) | in spec | 400 | 15 | high IMD order => OK
CA_n41C-n66A | CA_n41C | in spec | 190 | 5 | IMD5 MSD to be analyzed
CA_n41C-n71A | CA_n41C | in spec | 190 | 21 | high IMD order => OK
CA_n41C-n77A | CA_n41C | in spec | 190 | 9 | IMD9 MSD to be analyzed
CA_n41C-n79A | CA_n41C | in spec | 190 | 19 | high IMD order => OK
CA_n66A-n77(2A) | CA_n77(2A) | in spec | 600 | 5 | IMD5 MSD to be analyzed
DC_3A_n7B | DC_3A_n7B | flagFeb | 50 | 27 | high IMD order => OK
CA_n5B | CA_n5B | new | 25 | 3 | IMD3 MSD to be analyzed for intra-band basket
CA_n66(3A) | CA_n66(2A) | new | 70 | 11 | MSD to be analyzed for intra-band basket
CA_n66(A-B) | CA_n66B | new | 70 | 11 | MSD to be analyzed for intra-band basket
CA_n2(2A)-n30A-n66(2A) | CA_n2(2A) | new | 70 | 7 | IMD7 MSD to be analyzed
CA_n2(2A)-n30A-n66(2A) | CA_n66(2A) | new | 70 | 7 | IMD7 MSD to be analyzed
CA_n2(2A)-n30A-n66(2A) | CA_n2(2A) | new | 70 | 15 | high IMD order => OK
CA_n2(2A)-n30A-n66(2A) | CA_n66(2A) | new | 70 | 19 | high IMD order => OK
CA_n2A-n77(2A) | CA_n77(2A) | new | 600 | 7 | IMD7 MSD to be analyzed
DC_3A_n41C | DC_3A_n41C | new | 190 | 9 | IMD9 MSD to be analyzed
CA_n5A-n77(2A) | CA_n77(2A) | new | 600 | 11 | high IMD order => OK
CA_n30A-n77(2A) | CA_n77(2A) | new | 600 | 5 | IMD5 MSD to be analyzed
DC_41A_n79C | DC_41A_n79C | new | 200 | 19 | high IMD order => OK
DC_n46A-n48B | DC_n46A-n48B | new | 50 | 59 | high IMD order => OK
CA_n66A-n77(2A) | CA_n77(2A) | new | 600 | 5 | IMD5 MSD to be analyzed

## Slide 10: WF: Handling of existing and flagged combinations in this meeting
Analysis have been provided in thread 106
The cases in green can be introduced in the spec
The cases in yellow need to provide MSD proposals or technical justification for no MSD
The cases in red do not have the UL CA introduced, they are not allowed
DL configuration | Agreed UL configuration | Flagged UL configuration | IMD BW [MHz] | IMD order
CA_n2A-n77C | CA_n2A-n77A | CA_n77C | 200 | 15 (OK)
CA_n2(2A)-n77C | CA_n2A-n77A | CA_n77C | 200 | 15 (OK)
CA_n5A-n77C | CA_n5A-n77A | CA_n77C | 200 | 27 (OK)
CA_n5(2A)-n77C | CA_n5A-n77A | CA_n77C | 200 | 27 (OK)
CA_n48B-n66A | CA_n48A-n66A | CA_n48B | 40 | 15 (OK)
CA_n66A-n77(2A) | CA_n66A-n77A | CA_n77(2A) | 600 | 5
CA_n66(2A)-n77(2A) | CA_n66A-n77A | CA_n77(2A) | 600 | 5
CA_n66A-n77C | CA_n66A-n77A | CA_n77C | 200 | 13 (OK)
CA_n66(2A)-n77C | CA_n66A-n77A | CA_n77C | 200 | 13 (OK)
CA_n66B-n77A | CA_n66A-n77A | CA_n66B | Not in spec | CA_n66B UL needed
CA_n66B-n77C | CA_n66A-n77A | CA_n66B | Not in spec | CA_n66B UL needed
CA_n66B-n77C | CA_n66A-n77A | CA_n77C | 200 | 13(OK)

## Slide 11: References:
[1] R4-2107345 Inter-band ULCA with more than 2CCs, Qualcomm Incorporated, R4#98bis-e
[2] R4-2106908 FR1 CA/DC band combinations not for block approval, Apple, R4#98bis-e
[3] R4-2104818 Handling of Inter-band UL Configuration Including NR Intra-band ULCA, Skyworks Solutions Inc., R4#98bis-e
[4] R4-2104507 DraftCR for NR inter band CA DC combinations for 2DL with up to 2 bands UL, Verizon Denmark, R4#98bis-e
[5] R4-2103097 Way forward on introduction of NR intra-band UL CA as UL configuration in an inter-band combination, Skyworks Solutions Inc., RAN4#98e
[6] RP-210892 WF on guidelines for Rel-17 FR1 CA/DC band combinations approval handling, Apple Inc., Skyworks Solutions Inc., RAN#91e