## Slide 1: Way forward on analysis and framework of LB-LB-LB combinations
MediaTek, […etc.]
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105337
Electronic Meeting, Apr. 12 -20, 2021

## Slide 2: Background
DC_8-20_n28 was requested in RANP#90 and start discussion in RAN4#98-e meeting.
Concern was raised for three or more bands combination in nearby frequency range and with two UL in low band range (DC_8-20_n28)
Reference architecture in TR 36.715-03-01
CA_1A-3A-11A is another example for mid-band range

## Slide 3: Background:
880
915
925
960
791
821
832
862
703
748
758
803
n28
B20
B8
C-IM5
MSD on B8 due to TX IMD of n28+B20
UL DC IMDs interfering with other bands and creating band protection or MSD issues
Antenna design challenge: There are total 257MHz passband below 1GHz
Filter design challenge: feasibility of triplexer/quadplexer or hexaplexer while still need to meet single band requirements
TX IMD-x to other bands

## Slide 4: Proposed Way Forward
Inter-band CA/DC with three or more bands below 1 GHz with one or two UL bands within the frequency range is agreed to add to the list not for block approval
  Example: DC_8-20_n28
Inter-band CA/DC with two bands below 1 GHz with two UL bands within the frequency range is agreed to add to the list not for block approval
  Example: DC_20_n28 CA_n18-n28
Inter-band CA/DC with three or more bands between 1~2.2 GHz with one or two UL bands within the frequency range is agreed to add to the list not for block approval
  Example: CA_1A-3A-11A
Inter-band CA/DC with two immediately closed bands with one or two UL bands within the same frequency range is agreed to add to the list not for block approval
  Example: B3+39, B20+28 DC_2_n25
Discussion on feasibility and MSD requirement for combinations agreed to add to the list not for block approval to provide framework of discussion paper using DC_8-20_n28 as example

## Slide 5: Proposed Way Forward
Companies are encouraged to provide analysis/discussion for the combinations added to the list not for block approval
  Architecture feasibility
  Antenna design
  Front-end component feasibility
  MSD analysis (due to close proximity, TX IMD, TX C_IM-x…etc)
    other architecture not listed in TR36.715-03-01 is not precluded for MSD analysis
  TX emission and co-existence analysis
  Other analysis are not precluded

## Slide 6: References
[1] TS36.101
[2] R4-2101547 TP for TR 37.717-21-11: DC_8-20_n28
[3] R4-2104650 On support of DC_8-20_n1, DC_8-20_n3 and DC_8-20_n28
[4] TR 36.715-03-01