## Slide 1: WF on single UL intra-band ENDC REFSENS Exceptions
Skyworks, T-Mobile USA, CHTTL, […]
­­­3GPP TSG-RAN WG4 Meeting # 98-bis R4-2105338
Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Background
For Intra-Band (IB) Non-Contiguous (NC) EN-DC: REFSENS exceptions tables do not capture the Aggressor/Victim (Agg./Vict.) landscape for bands like n71 where UL/DL are inverted [1].
  To fix EN-DC tables, proposal to either adopt new tables or correct current tables is made [1]. If table correction is preferred, further improvements are proposed in [1] to prevent footnote expansion and to ensure some alignment with NCCA tables,
  MSD test points for NC EN-DC REFSENS do not always maximize MSD [1]. It was proposed to adopt fully allocated Agg. UL configuration. This raises several options on addressing MSD concerns:
For IB FDD NCCA,
  Aggregated CBW are expressed in units of [RB]s for PCC+SCC. Correction to use [MHz] instead is proposed in [1],
  Agreement was reached to prevent specifications expansion that results from specifying an MSD test point for each possible CBW permutations [2]. MSD for CA_n25(2A) was implemented according to these guidelines, but it seems CA_n71(2A) was not. This raises several questions:
    Is this agreement only applicable to IB NCCA or is-it also applicable to IB NC EN-DC combinations?
    Should previously agreed MSD test points be re-visited to ensure consistency?
    For NC EN-DC: can further optimization of specifications be considered to address the permutations of Agg./Vict. ?
Options | Pro | Cons
1-1: Keep legacy small Agg. RB allocations | No impact on previous agreements | MSD may be under-estimated. We remain dependent on IMD landscape for future combinations
1-2: Adjust small Agg. RB allocations to ensure highest order IM/C-IM maximizes MSD | Worst-case MSD is captured | Dependency on IMD landscape remains for future combinations May require revisiting previously agreed test points.
1-3: Adopt fully allocated Aggressor UL configurations | Worst/close to worst case MSD is captured Removes dependency on IM landscape | Eventhough fully allocated Agg. UL configuration may occur due to un-coordinated NR and LTE schedulers, this scenario may not reflect the assumption of co-located eNb/gNbs. Single carrier REFSENS small RB allocations remains a valid assumption.

## Slide 3: Background: Table Structure Issue [1]
Fig. A & B show the current table concept: they are designed for DL band above UL band, eg. DC_3_n3.
DC_71_n71 is currently specified in Fig B. Table 7.3B.3-2-2, a table which does not work for n71 (Fig C),
Note that REFSENS exceptions due to Aggressor/Victim permutation are not systematically specified, eg. DC_71A_n71A

## Slide 4: Background: Small Allocations Under-estimated MSD [1]
Fig. A: Agreed MSD corresponds to LTE being victim of NR 5RB9 IMD7 test point, leading to ΔRIBNC = 4.3dB, (cf. option 1-1,background slide)
Fig. B: Measured MSD corresponds to LTE being victim of NR 3RB0 IMD5 test point, leading to ΔRIBNC = 6.8dB, (cf. opt. 1-2)
Fig. C: Measured MSD corresponds to LTE being victim of NR 50RB0 (full-allocation), leading to ΔRIBNC = 21.6dB, (cf. opt 1-3)

## Slide 5: Background: Guidelines to Prevent Specifications Expansion [2]
RAN4 agreed to adopt the following principles for IB NCCA [2]
  Only 1 test configuration is defined for each band.
  It is specified at PCC+SCC= 25RB + 25RB and SCS 15kHz, and maximum Wgap
Note that:
  For CA_n71(2A), the agreed test points seem to deviate from this guideline,
  For R4-2104425 DC_71A_n71A TP [3]:
    it was observed during off-line discussions that adding a test point for new BCS1 30MHz aggregated BW is an identical IMD landscape than the agreed test point for BCS0 25MHz Agg. BW.
    Following guidelines from [2], it may be considered it is not necessary to introduce an additional test point for 30MHz Agg. BW since, from an RF test perspective, no new information is captured.

## Slide 6: WF on Addressing Table Structure
1) Accommodating bands where UL band is above DL band in NC EN-DC tables 7.3B.3.2-1 and 7.3B.3.2-2:
Do not introduce new tables,
  Corrections to Table 7.3B.3.2-1:
    Adopt title:
    “Intra-band non-contiguous EN-DC with one uplink configuration on E-UTRA for reference sensitivity (E-UTRA uplink carrier is closer to higher than the NR downlink carrier than it is to the E-UTRA downlink carrier)”,
    Adopt Footnote 3:
    “Note 3: The E-UTRA uplink carrier is the aggressor and The table only applies when the center frequency of E-UTRA carrier is higher than the NR carrier, and, the ΔRIBNC applies to the NR DL carrier only. The E-UTRA uplink carrier shall be located as close as possible to the NR downlink carrier centre frequency.”
  Corrections to Table 7.3B.3.2-2:
    Adopt title:
    “Intra-band non-contiguous EN-DC with one uplink configuration on NR for reference sensitivity (NR uplink carrier is closer to higher than the E-UTRA downlink carrier than it is to the NR downlink carrier)”
    To remove ambiguity on NR aggressor SCS specification, adopt footnote 3:
    “Note 3 : The NR uplink carrier is the aggressor and The table only applies when the center frequency of NR carrier is higher than the E-UTRA carrier, and, the ΔRIBNC applies to the E-UTRA DL carrier only. The NR uplink carrier shall be located as close as possible to the E-UTRA downlink carrier center frequency. The NR SCS should be the smallest SCS that is compatible with the highest uplink channel bandwidth.”
2) Options for improvements to ENDC REFSENS tables:
  RBstart is removed from footnotes and is captured in the “Aggressor UL NR allocation” column, (see Appendix I)
3) For IB NCCA tables:
  Replace Aggregated Channel Bandwidth (PCC+SCC) in [RB]s with values in [MHz].
  Remove RBstart from footnotes and capture in the column "UL PCC allocation"

## Slide 7: WF on Addressing Under-Estimated MSD
1) For new BCS / IB NC EN-DC combinations
  Adopt small/medium Lcrb UL aggressor configurations which maximize the victim’s MSD for all new ENDC combinations or new EN-DC BCS in REL-17.

## Slide 8: Recommendations on Preventing Specification Expansion
Addressing IB NC EN-DC specification complexity due to all CBW permutations:
Option 1:
  Specify only 1 test point per maximum Aggregated CBW,
  The test point configuration is specified at SCS15kHz for:
    The maximum Wgap only [2],
    The lowest victim CBW only,
    The maximum victim’s MSD, i.e. the test points ensure the highest IM/C-IM order collision occurs,
    To ensure each CBW is specified and each BCS specified, it is not precluded to adopt one test point that corresponds to an identical IM collision landscape of another CBW. For example, we can have one test point for BCS0 25MHz Agg. BW and one test point for say BCS1 30MHz Agg. BW which both correspond to the same IMD product.
Option 2:
  Specify only 1 point per band at SCS 15kHz that correspond to the worst case MSD and Wgap maximum.
Other options are not precluded (e.g. maintain the existing approach in the spec)
2) Handling of deviations from [2] for NCCA
Option 1: Correct combinations which do meet the agreement [2], eg. CA_n71(2A),
Option 2: Adopt the above “option1” IB NC ENDC guideline, i.e., for each band, tolerate the introduction of 1 test point per Aggregated CBW.

## Slide 9: Recommendations on Preventing Specification Expansion
3) Addressing cases of ΔRIBNC = 0 for all ENDC CBW permutations (eg. DC_7A_n7A):
Specify only 1 table entry and use Notes 4, 8, 9 similar to DC_66A_n66A specifications.
4) Addressing IB NC ENDC specification complexity due to Aggressor / Victim permutations:
  Option 1:
    Statut-quo: keep on specifying Agg/Vict permutations.
    FFS how to handle combinations which have been specified in one table only,
  Option 2: Only specify REFSENS exceptions where the victim is the anchor point,
  Option 3: Considering the small differences in single carrier REFSENS levels between LTE and NR, FFS other solutions that reduce the specifications complexity. The MSD difference between LTE and NR victim may be small,

## Slide 10: References
# | TDoc | Title | Source
1 | R4-2107338 | Intra-band REFSENS Exceptions for n71 | Skyworks Solutions Inc.
2 | R4-1908552 | Handling of NR FDD band NCCA REFSENS requirements | MediaTek Inc.
3 | R4-2104425 | TP to TR 37.717-11-11: DC_71A_n71A | Nokia, T-Mobile USA

## Slide 11
Appendix I: Example of corrections for Table 7.3B.3.2-2
Illustration of title, table and footnote changes from WF on Addressing Table Structure [slide 6] for Table 7.3B.3.2-2
.
.
.

## Slide 12
Appendix II:NCCA Table 7.3A.2.2-1 corrections
Example Table 7.3A.2.2-1 corrections:
  Replace units of [RB]s with units of [MHz]
  Remove RBstart from footnotes and capture in the column "UL PCC allocation"

## Slide 13
Appendix III: Example of MSD test point simplification
Example of simplification
keeping legacy test points, and
removing test points where Wgap is <maximum Wgap