## Slide 1: WF on adding 90 and 100MHz channel BW for UE in band n40
Huawei, HiSilicon, CMCC
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105360 Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Status summary for 1st round discussion[4]
 | Status summary
Sub-topic#2-1 | Sub-topic: Introduction of 90 and 100MHz channel BW 3 companies are for option 2, limiting UL channel to 80MHz as it would solve the issues with 90/100Mhz, while 2 companies are willing to introducing 90 and 100MHz. Considering also the other comments on sub-topic 1-2, it might be acceptable to still introduce 90 and 100 MHz but with additional restrictions (specifying delta MPR, adpated co-existence requirements with n41, …) Tentative agreements:Introduce 90 and 100 MHz channel BW, considering specifying Δ -MPR, new co-existence requirements with n41, or even A-MPR. Candidate options: Recommendations for 2nd round: Continue discussions and the other sub-topics to finalize this tentative agreement and capture in the WF.
Sub-topic#2-2 | Sub-topic: Δ-MPR As compromise of adding 90 and 100MHz channel BW, following tentative agreement seems acceptable: Tentative agreements:Introduce Δ-MPR for 90 MHz and 100MHz. Candidate options:For 90MHz channel BW: 0.5dB (assuming -40dBm/MHz coex limit) For 100MHz chanel BW: 2dB(assuming -40dBm/MHz coex limit) or 1dB (PC2 and PC3) Recommendations for 2nd round: Continue discussion on the 2 options and capture agreement in the WF.
Sub-topic#2-3 | Sub-topic: Co-existence with n41 limit As compromise of adding 90 and 100MHz channel BW, following tentative agreement seems acceptable: Tentative agreements: Specify coexistence limit with n41: -40dBm/MHz Candidate options:This limit will be applicable: Option1: On the full band for 90 and 100MHz. Option2: Only in 2496MHz-2505MHz, the -50dBm/MHz would be applicable in the rest of the band, i.e. 2505MHz-2690MHz Recommendations for 2nd round: : Continue discussion on the 2 options and capture agreement in the WF.

## Slide 3: WF
  Introduce 90 and 100 MHz channel BW, considering specifying Δ -MPR, new co-existence requirements with n41.
    Option 1: Restrict UL RBs to max 80MHz aggregated BW. RBs might be placed at lower frequency edge of channel (Δ-MPR is not required)
    Option 2: No restriction to UL RBs
  Introduce Δ-MPR for 90 MHz and 100MHz.
    Option 1: For 90MHz channel BW: 0.5dB (assuming coexistence limit option1)
    For 100MHz chanel BW: 2dB (assuming coexistence limit option1)
    Option 2: 1 dB
  Specify coexistence limit with n41: -40dBm/MHz which will be applicable:
    Option 1: on the full band
    Option 2: only in 2496MHz-2505MHz, and -50dBm/MHz would be applicable in the rest of the band, i.e. 2505MHz-2690MHz

## Slide 4: Reference
[1] R4-2104880, Discussion on new CBW 90MHz and 100MHz for n40, Apple
[2] R4-2106480, Adding 90 and 100MHz bandwidth for band n40 Huawei, HiSilicon, CMCC
[3] R4-2107324, n40 90M 100M BWs, Qualcomm Incorporated
[4] R4-2105185, Email discussion summary for [98-bis-e][112] NR_bands_R17_BWs, Moderator (Ericsson)