## Slide 1: Possible improvements on MSD in relation to BCS4
Huawei, HiSilicon, Skyworks Solutions Inc.
3GPP TSG-RAN WG4#98bis-e R4-2105373
Electronic Meeting, April 12 – 20, 2021

## Slide 2: Background
In the objective 2 of WID [1], RAN4 need to analysis all required MSD for every existing band combination to enable BCS4 if the BCS4 is applicable for all the band combinations.
For inter-band CA and SUL band combinations, the reference sensitivity exceptions due to harmonic interference and cross band isolation are specified as bandwidth-specific requirements. As more and more kinds of bandwidth for single carrier are specified in the spec, the following issues are brought into specifications for MSD exceptions.
  After the completion of new bandwidth for single carrier, RAN4 have to check the MSD exceptions for all the relative band combinations and fill up the missing requirements.
  In Rel-17, RAN4 will introduce 15 channel bandwidths (5, 10, 15, 20, 25, 30, 35, 40, 45, 50, 60, 70, 80, 90, 100) for FR1. Considering that the existing UE RF MSD exception tables with channel bandwidth dependency is already fairly crowded.
  It’s inconvenient to maintain the MSD exception tables as the channel bandwidths are increasing.
  There are still some missing requirements and errors in the MSD exception tables.
MSD due to the IMD interference from 2UL band is not considered in this WF.

## Slide 3: WF on MSD due to harmonic interference
1) MSD levels:
Option 1: To consider a equation-based approach per band combination for different DL channel bandwidths and some assumptions and issues are listed as below
  The victim's RX CBW entirely overlaps the aggressor's UL harmonic,
  The victim’s receiver integrates the total power of the PA harmonic PSD ,
  FFS whether the interference is equal on all RX ports or not based on the architecture
  FFS in case of partial overlap/near miss cases.
Option 2: Keep the traditional way
Option 3: Other solutions are not precluded.

## Slide 4: WF on MSD due to harmonic mixing interference
2) Aggressor UL allocations
Option 1: Specify the aggressor’s UL RB allocation so that the UL harmonic is entirely contained within the victim’s smallest Rx CBW. Use this Lcrb for all victim’s Rx CBW greater than the minimum CBW.
Option 2: Keep the existing table
Option 3: Other solutions are not precluded.
3) Guidelines on MSD due to Rx harmonic mixing:
Option 1: Specify only
for victim's Rx carrier frequency < 2GHz:
- victim's harmonics to considered: H1,H3,H5, say harmonic order "m“
- aggressor harmonics to be considered: H1,H2,H3,H4,H5, say harmonic order "n"
- cases where n+m<= 5
for victim's Rx carrier frequency >=2GHz:
- victim's harmonics to considered: H1,H2,H3,H5, say harmonic order "m“
- aggressor harmonics to be considered: H1,H2,H3,H4,H5, say harmonic order "n"
- cases where n+m<= 5
Option 2: Other solutions are not precluded.

## Slide 5: WF on MSD due to cross band isolation
There are three cases to be considered for different UL Tx bandwidths, DL Rx bandwidths and frequency gap between UL and DL carrier frequencies
  Case 1: Tx ACLR1 is overlapping with the Rx DL channel.
  Case 2: Tx ACLR2 is overlapping with the Rx DL channel without Tx ACLR1 overlapping.
  Case 3: Others: the Rx CBW is neither victim of the aggressor’s Tx ACLR1 nor of the Tx ACLR2.

## Slide 6: WF on MSD due to cross band isolation
There are several factors to be determined for MSD test configuration
1) Carrier Frequencies
  Option 1: The UL and DL carrier frequencies should be configured to minimize the gap separating the DL victim carrier to the UL carrier frequency.
  Option 2: Others
2) UL Channel bandwidth
  Option 1: Highest uplink CBW that is specified for the aggressor band
  Option 2: Highest uplink CBW that UE supports for the aggressor band
  Option 3: More than one UL CBWs can be considered for different cases.
  Option 4: Others
3) UL RB allocation
  Option 1: Highest possible Lcrb that is compatible with the DFT-s-OFDM 2,3,5 radix rule for the highest UL CBW, ie. fully allocated UL configuration. (all the cases)
  Option 2: 25RB allocated on the edge of UL CC (Only for case 1 due to IM3/CIM3)
  Option 3: When the FDD and TDD aggressor share same MSD mechanism under same TX BW, one RB or fewer RBs for case 1 and 2 due to IM3/CIM3/IM5/CIM5
  Option 4: Others

## Slide 7: WF on MSD due to cross band isolation
4) UL SCS
  Option 1: When NR carrier is the aggressor, the NR SCS should be the smallest SCS that is compatible with the configured UL CBW.
  Option 2: When NR carrier is the aggressor, the NR SCS should be the smallest SCS that is compatible with the highest UL CBW.
5) DL Channel bandwidth
  Option 1: for all victim’s band specified CBW.
  Option 2: for all victim’s band specified CBW that UE supports for the band combination
  Option 3: Others
6) DL RB allocation
  Option 1: Fully allocated DL configuration corresponding to each victim’s downlink CBW.
7) DL SCS
  Option 1: The NR SCS should be the smallest SCS that is compatible with the DL CBW.

## Slide 8: References
# | TDoc | Title | Source
1 | RP-202832 | New WID: Introduction of bandwidth combination set 4 (BCS4) for NR | Ericsson, T-Mobile USA
2 | R4-2106677 | Discussion on how to simplify MSD definition using bandwidth-agnostic approach | Huawei, HiSilicon
3 | R4-2106678 | Discussion on MSD due to cross band isolation and counter intermodulations | Huawei, HiSilicon
4 | R4-2107322 | Impact of Large NR BW on Crossband MSD | Skyworks Solutions Inc.

## Slide 9: Appendix based on R4-2107322
The impact for different test configurations

## Slide 10: Appendix based on R4-2107322
Measured noise level in n3 5,10,15,20,25,30 MHz CBW vs n1 20,25,30,40,50 UL CBW. Left: n1 Lcrb=25 (RBstart=0), Right: n1 full RB allocation.
Measured noise level in n3 5,10,15,20,25,30 MHz CBW vs n1 20,25,30,40,50 UL CBW. Left: n1 Lcrb=25 (RBstart=0), Right: n1 full RB allocation.
Observations:
- For n1 CBW<=40MHz, neither C-IM5, nor the legacy cross-band isolation test point guarantee that the worst case MSD is specified. High MSD can be captured using full n1 RB allocations,
- For n1 CBW=50MHz, C-IM3 MSD is approximately 3dB higher than the 22.5dB MSD due to full allocation for n3 5MHz CBW. For n3 CBW >=20MHz, the MSD difference between the two types of allocations becomes insignificant.