## Slide 1: WF on PC2 UL MIMO for Band n40
Huawei, HiSilicon
R4-2105374
3GPP TSG-RAN WG4 #98-bis-e
Electronic Meeting, Apr. 12-Apr. 20, 2021

## Slide 2: Background
Issues during the discussion
  PC3 UL MIMO bands introduction needs to be proposed to a WID first before the CR process. Should we also follow the same process for PC2 UL MIMO bands introduction?
  What MPR requirements should be applied for PC2 UL MIMO bands?
  How to differentiate PC2 UL MIMO with the following three potential PA implementations: (26dBm + 26dBm), (26dBm + 23 dBm), (23dBm + 23dBm)?

## Slide 3: WF
PC3 UL MIMO bands introduction needs to be proposed to a WID first before the CR process. Should we also follow the same process for PC2 UL MIMO bands introduction?
Clarification
  For bands already support PC3 but not UL MIMO in the spec, request PC3 UL MIMO in the basket UL MIMO WI.
  For bands already support PC2 but not UL MIMO in the spec, request PC2 UL MIMO in the basket UL MIMO WI.
    No prerequisite that the band has to support PC3 MIMO firstly

## Slide 4: WF
What MPR requirements should be applied for PC2 UL MIMO bands?
Clarification
  Same MPR for TxD Same MPR for other bands supporting PC2 UL MIMO being discussed is applied for n40 to support PC2 UL MIMO

## Slide 5: WF
How to differentiate PC2 UL MIMO with the following three potential PA implementations: (26dBm + 26dBm), (26dBm + 23 dBm), (23dBm + 23dBm)?
Clarification
  No need to differentiate the PC2 UL MIMO requirements for different PA implementations.

## Slide 6: Way Forward
Introduce PC2 UL MIMO for n40 after the PC2 UL MIMO MPR requirements are completed.

## Slide 7
Reference
[1] R4-2105192, Email discussion summary for [98-bis-e][119] NR_intra_HPUE_UL_MIMO_bands, Huawei, HiSilicon