## Slide 1: WF on UE RF requirement for FR2 HST
Samsung
3GPP TSG-RAN WG4#98-bis-e Meeting R4-2105398
Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Way Forward – UE RF Requirement Framework
Further discuss on RF requirement framework for FR2 HST UE:
  FFS multiple RF requirement sets based on different scenarios or different implementations

## Slide 3: Way Forward – Minimum Peak EIRP
Antenna elements per panel
  Baseline for requirement derivation: 4x4 with two polarization, TRP max = 23dBm
  Other options are not precluded.
Minimum peak EIRP derivation
  Option 1: Deciding EIRP based on number of antenna element following PC5 discussion (R4-2011870):
    4x4 antenna elements per panel with 30.X dBm min peak EIRP
    Other antenna elements assumptions, including 8 elements with up to 28.3dBm min peak EIRP
  Option 2: From UE implementation perspective, companies are encouraged to provide technical input based on the below table to derive minimum peak EIRP

## Slide 4: Table. Template for minimum peak EIRP
Parameter | Unit | Freq. range 24.25-29.5 GHz
P_out per element | dBm | TBD
# of antennas in array |  | TBD
Total conducted power per polarization | dBm | TBD
Avg. antenna element gain | dBi | TBD
Antenna roll-off loss vs frequency | dB | TBD
Realized antenna array gain | dBi | TBD
Polarization gain | dB | TBD
Mismatch and transmission line loss including load pull | dB | TBD
Beam forming loss (phase shifter and amplitude error) | dB | TBD
Finite beam table | dB | TBD
Beam forming loss (one beam table fits all) | dB | TBD
Form-factor integration losses | dB | TBD
Total implementation loss (worst-case) | dB | TBD
Peak EIRP (Minimum) | dBm | TBD
TRP (to be compared with TRP limit) | dBm | TBD

## Slide 5: Way Forward – Spherical Coverage Requirement
For spherical coverage requirement, FFS
  The x%-tile point in EIRP CDF:
    # of panels, # of beams in beambook and x%-tile point need to consider how much spherical coverage is needed, based on deployment scenario analysis.
  FFS different x%-tile point needed for different scenarios.
  FFS detailed requirement for minimum EIRP value at x%-tile.

## Slide 6: Way Forward – Beam Correspondence
Beam Correspondence requirement for FR2 HST UE:
For Rel-15 Beam Correspondence:
  Option 1 (Samsung/Qualcomm/Ericsson/ZTE/Nokia): BC bit-0 UE is not allowed, i.e., UE shall meeting the minimum peak EIRP requirement and spherical coverage requirement with its autonomously chosen UL beams and without uplink beam sweeping.
  Option 2 (Huawei): No need to mandate FR2 HST UE support BC bit-1.
For Rel-16 Beam Correspondence:
  FFS the necessity of support Rel-16 optional feature beamCorrespondenceSSB-based-r16
  FFS the necessity of support Rel-16 optional feature beamCorrespondenceCSI-RS-based-r16

## Slide 7: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2104906 | On FR2 HST RF Requirements | Qualcomm, Inc.
R4-2104585 | Consideration on UE beam and pwr requirements for FR2 HST | Ericsson France S.A.S
R4-2104719 | UE power class for FR2 HST | Nokia, Nokia Shanghai Bell
R4-2105026 | On baseline power class and UE RF requirement for FR2 HST | Samsung
R4-2104586 | Considerations on Beam correspondence for HST FR2 UEs | Ericsson France S.A.S
R4-2104720 | UE beam correspondence for FR2 HST | Nokia, Nokia Shanghai Bell
R4-2106333 | On Beam Correspondence Requirement for FR2 HST UE | Samsung

## Slide 8: Reference
[1] R4-2105470, “Email discussion summary for [98-bis-e][133] NR_HST_FR2_enh”, Samsung