## Slide 1: WF on general principle for SL enhancement in Rel-17
Agenda item: 8.10.1
Source: LG Electronics
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105400
Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Background
In RAN4#98-bis-e, RAN4 discussed some general principle for SL enhancement requirements.
  Issue 1-1-2: How to define new operating bands and RF requirements for SL enhancement in Rel-17
  Issue 1-1-3: Terminology of partially used licensed band between SL and Uu operation
  Issue 1-1-4: How to apply Release independent manner for public safety service, intra-band con-current operation and PC2 SL UE
  Issue 1-2-1: Channel raster & Sync. Raster
  Issue 1-2-2: Max. CBW for SL operation in licensed band
  Issue 1-2-3: CBW for n14 SL operating band
The new feature in the SL enh (public safety service & other WG led issues) are in-scope in rel-17 SL enh. WID.
Also, RF perspective, the Rel-16 left over issues (Intra-band V2X/ intra-band con-current V2X operation, TxD for V2X and PC2 V2X) are included in Rel-17 SL enh. WI based on agreed work plan.
All the features for SL enhancement (SL enh & left over issues) are optional
From e-mail discussion, RAN4 make consensus to define general principle for above open issues.

## Slide 3: WF: How to define new operating bands and RF requirements
In RAN4 e-mail discussion, moderator proposed two options as follow
  Issue 1-1-2: How to define new operating bands and RF requirements for SL enhancement in Rel-17
    Option 1: Make new suffix to define new operating bands for SL enhancement service including Public safety service and other commercial SL operation.
    Option 2: Reuse suffix E to add new operating bands for SL enhancement. Also add general descriptions to cover all SL operation in suffix E in clause 4.3 in TS38.101-1.
  Based on e-mail discussion, RAN4 agreed the general principle how to define the SL enhancement operating band and RF requirements as follow
Agreement: Option 2

## Slide 4: WF: Terminology of partially used licensed band
In RAN4 e-mail discussion, moderator proposed two options as follow
  Issue 1-1-3: Terminology of partially used licensed band between SL and Uu operation
    Option 1: Use the ‘intra-band con-current V2X operating bands’ instead of ‘licensed bands partially used for SL.
    Option 2: Other option is not precluded
  Based on e-mail discussion, RAN4 agreed to use the terminology with “intra-band con-current V2X operating bands” for partially used licensed bands with FDM and “intra-band V2X operating bands” for partially used licensed bands with TDM as follow
Agreement: Option 1.

## Slide 5: WF: Release independent principle
In RAN4 e-mail discussion, proposed 4 options as follow
  Issue 1-1-4: How to apply Release independent manner for public safety service, intra-band con-current operation and PC2 SL UE
    Option 1: All of objectives (SL enh, & left over issues) for SL enh. operation in Rel-17, will be supported from Rel-16 as release independent principle.
    Option 2: SL enh. operation in Rel-17 will be supported from Rel-17, and other left over issues will be supported from Rel-16 as release independent principle.
    Option 3: All of objectives (SL enh, & left over issues) for SL enh. operation in Rel-17, will be supported from Rel-17 as release independent principle.
    Option 4: Other option is not precluded
  Based on e-mail discussion, RAN4 agreed to apply the release independent principle for SL enh. In Rel-17 as follow
Agreement: Option 2 with the pre-condition that no signaling impact for Rel-16 left over issues.

## Slide 6: WF: System parameters
In RAN4 e-mail discussion, channel raster & sync. Raster issues are discussed as follow
  Issue 1-2-1: Channel raster & Sync. Raster
    Option 1: Reuse the general channel raster and sync raster for NR Uu in Rel-16 for SL enhancement operation in licensed band.
    Option 2: Follow NR SL channel raster (15kHz channel raster in n47) in SL enh. NR operating band.
  Based on e-mail discussion, RAN4 agreed to reuse the general channel raster and sync. Raster for NR Uu in licensed band as follow
Agreement: Option 1.

## Slide 7: WF: Max. CBW for SL enh.
In RAN4 e-mail discussion, max. CBW for SL enh. Operating bands in licensed bands are discussed as follow
  Issue 1-2-2: Max. CBW for SL operation in licensed band for NR V2X
    Option 1: It is proposed that the max CBW for SL service for NR V2X in licensed band is limited to 40MHz
    Option 2: The max. CBW for SL service for NR V2X is up to operator request in licensed bands
    Option 3: other option is not precluded
  Based on e-mail discussion, RAN4 agreed that the max. CBW is limited 40MHz in licensed band.
Agreement: Option 1

## Slide 8: WF: Channel BWs for SL enh.
In RAN4 e-mail discussion, CBW for SL enh. Operating bands in licensed bands are discussed as follow
  Issue 1-2-3: CBW for n14 SL operating band
    Option 1: It is suggested to support both 5MHz and 10MHz channel bandwidths in n14 for SL transmission.
    Option 2: Only support 10MHz Channel bandwidth
  Based on e-mail discussion, RAN4 agreed to support both 5MHz and 10MHz CBW in n14 SL enhancement.
Agreement: Option 1.

## Slide 9: Reference
R4-2105207, “RAN4#98-bis-e_summary_134_NRSL_enh_part1,” Moderator (LG Electronics)
R4-2104529, “Discussion on system parameters for newly introduced SL bands,” vivo
R4-2107305, “On CBW for licensed band supporting NR V2X,” Huawei
R4-2104775, “TP on CBW and system parameters for newly introduced SL bands,” CATT
R4-2104971, “TP on operating scenarios for NR SL enhancements in Rel-17,” LG Electronics