## Slide 1: WF on operating scenarios for SL and Uu in the same licensed band
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, 12th - 20th April, 2021
Agenda item: 8.10.5
Document for: Approval
R4-2105403
CATT, …

## Slide 2: Issue 1-1-1: Whether to narrow down operating scenarios
  Candidate options:
  Option 1: RAN4 needs to narrow down the operation modes for intra-band con-current operation.
    Option 1a: Consider the following two cases for intra-band con-current operation:
      Case 1: SL and Uu are in the same carrier with different BWPs
      Case 2: SL and Uu are in different carriers
  Recommended WF:
  Focus on prioritization on operating scenarios including TDM and FDM.
    1st priority: TDM
    2nd priority: FDM with adjacent carrier
    3rd priority: FDM with non-adjacent carrier

## Slide 3: Issue 1-1-2: Other operating scenario
  Agreement:
  Scenario 2 in R4-2106554 is not in Rel-17 SL enhancement WI scope. Inter-band con-current operation can be treated in Rel-17 basket WI of NR_LTE_V2X_PC5_combos.

## Slide 4: Issue 1-1-3: Full duplex or half duplex
  Recommended WF:
  Clarify the meaning of full duplex and half duplex for SL and Uu within the same licensed band together with operating scenarios.

## Slide 5: Issue 1-2-1: TDM operating scenarios
  Agreement:
  RAN4 allow TDM operation between spectrally partially used PC5 SL and Uu UL/DL operation in a licensed TDD band regardless of adjacent/ non-adjacent carrier (Option 1 as the majority view in 1st round).

## Slide 6: Issue 1-3-3: Time mask
  Candidate options:
  Option 1: Consider the time mask for SL and Uu switching in paper R4-2104777.
  Option 2: Define similar time mask as Uplink TX switching with capability signaling of SidelinkSwitchingPeriod.
  Recommended WF:
  Postpone until sync mechanism between SL and Uu is clear.

## Slide 7: Issue 1-4-2: Frequency separation for non-adjacent carriers
  Candidate options:
  Option 1: For the FDD/TDD intra-band con-current operation with non-adjacent carrier, RAN4 need further discussion on the detail coexistence scenarios based on operator deployment scenarios and request.
  Option 2: No need to introduce the frequency separation for the case Uu and SL are in different channels for intra-band con-current operation.
  Option 3: To study the frequency separation in non-adjacent channel, the frequency separation between existing UL and DL of FDD bands can be considered as a starting point.
  Recommended WF:
  Focus on prioritization on operating scenarios including TDM and FDM before decide whether to need frequency separation for non-adjacent carriers.

## Slide 8: Issue 1-6-1: UE RF architecture
  Candidate options:
  Option 1: The separate RF architecture should be considered as baseline to derive the RF requirements for partial usage between NR V2X and NR Uu in licensed band.
  Option 2: Choose which of following approach is adopted for scenario 1 (NR Uu and SL supported by UE in same band) in requirement definition.
      Alt 1: Only define requirements for separate RF chain architecture
      Alt 2: Only define requirements for the worst case, i.e. single RF architecture
      Alt 3: Define requirements for both and rely on UE capability to indicate which requirements it follows
  Option 3: Decide UE RF architecture based on specific operating scenario.
  Recommended WF:
  Determine basic RF architecture for different operating scenarios. Other RF architecture is not precluded from implementation perspective.
    1st priority: TDM (Single RF chain for Tx as baseline)
    2nd priority: FDM with adjacent carrier (Separate RF chain as baseline)
    3rd priority: FDM with non-adjacent carrier (Separate RF chain as baseline)

## Slide 9: Reference
[1] R4-2105326, Email discussion summary for [98-bis-e][135] NRSL_enh_Part_2, Moderator (CATT), RAN4#98-bis-e