## Slide 1: Way forward on PC2 NR V2X
Huawei, HiSilicon, LG Electronics
R4-2105407
3GPP TSG-RAN WG4 #98-bis-e
Electronic Meeting, Apr. 12-Apr. 20, 2021

## Slide 2: Background
The following issues related to PC2 NR V2X have been discussed in RAN4#98-bis-e meeting
  Topic #1: Issues related to PC2 HPUE for SL enhancements
    Issue 1-1: Handling of SL-MIMO and TxD for NR V2X
    Issue 1-2: NR V2X PC2 power class capability
    Issue 1-3: Upper bound of power class for inter-band con-current HPUE and associated requirements
  Topic #2: MPR/A-MPR evaluation
    Issue 2-1: MPR/A-MPR simulation results
  Topic #3: Co-existence study
    Issue 3-1: Co-existence evaluation for Uu and SL
    Issue 3-2: Co-existence evaluation for SL only
    Issue 3-3: Co-existence study for n38 (SL) and adjacent band n7 (Uu)
    Issue 3-4: Other co-existence issues

## Slide 3: WF
Issue 1-1: Handling of SL-MIMO and TxD for NR V2X
Agreement
  It is agreed to define the SL-MIMO and NR SL with TxD requirements respectively under the V2X suffix E and use same set of MPR for SL-MIMO and TxD.

## Slide 4: WF
Issue 1-2: NR V2X PC2 power class capability
Options
  Option 1: Specific PC2 power class for NR V2X needs to be defined.
  Option 2: No need to introduce Specific PC2 power class for NR V2X
WF
  To be further discussed

## Slide 5: WF
Issue 1-3: Upper bound of power class for inter-band con-current HPUE and associated requirements
Agreement
  Power control for V2X SL and Uu are separate therefore No upper bound of power class is needed for inter-band con-current operation.

## Slide 6: WF
  Issue 2-1 : MPR NR V2X
Agreement
  To be further discussed and encourage to provide MPR requirements from interested companies
  Issue 2-2 : A-MPR NR V2X
Agreement
  For A-MPR based on FCC regulation, it is agreed to further check the FCC regulation and corresponding A-MPR requirements for PC3. The issue will be discussed in Rel-16 TEI maintenance for PC3 firstly.

## Slide 7: WF
Issue 3-1: Co-existence evaluation for Uu and SL
Agreement
  It is agreed to conclude that with power control, Uu and SL can co-exist well in licensed band for PC2 V2X UE.
  It is agreed to specify 31 dBc ACLR requirement for PC2 NR V2X UE based on co-existence study.
  For regulatory aspect to allow high power UE, RAN4 need to check the regional regulatory requirements to allow PC2 V2X UE in licensed bands.

## Slide 8: WF
Issue 3-2: Co-existence evaluation for SL only
Agreement
  It is agreed to conclude that PC2 NR V2X UE can co-exist well with NR V2X system.

## Slide 9: WF
Issue 3-3: Co-existence study for n38 (SL) and adjacent band n7 (Uu)
Options
  Option 1: Study A-MPR for PC2 V2X UE in n38 to protect NR UE operating in n7 and LTE UE in B7
  Option 2: Study co-existence of PC2 V2X UE in n38 (SL) with n7 (Uu) once the PC2 NR Uu is supported in band n38.
WF
  To be further discussed

## Slide 10: WF
Issue 3-4-1: Whether need to update PEMAX,c for scenario of Uu and SL co-existence
Agreement
  It is agreed to update PEMAX,c for scenario of Uu and SL co-existence. Detailed changes need further discussion.

## Slide 11: WF
Issue 3-4-2/3/4: Co-channel co-existence issues
Options
  Option 1: Continue the discussion of co-channel co-existence, but the scenarios and issues to be discussed need to be clarified.
  Option 2: Co-channel co-existence is not in the scope of the WID. No need to have further discussion.
WF
  To be further discussed

## Slide 12
Reference
[1] R4-2105209, Email discussion summary for [98-bis-e][136] NRSL_enh_Part_3, Huawei, HiSilicon